## Slide 1: Overview Objective 3
Objective: Relate Principles Pertaining to Internet Protocol (IP) Addressing and Subnetting.
  Evaluation
    Written Test / Training Mission
  Learning outcomes
    Explain the decimal, binary, & hexadecimal number systems & perform conversions
    Explain IPv4 addressing, classes, & perform subnetting
    Identify facts about & perform Variable Length Subnet Masking (VLSM)
    Identify facts about IPv6
    Identify facts about Network Address Translation (NAT)

## Slide 2: Boolean Logic
Boolean logic is a branch of algebra that uses logical operators
  Useful to computers because they calculate in binary: 1s or 0s
  “AND” logic is used in subnet masks
  “OR” logic is used in wildcard masks
0
0
0
1
0
0
0
1
0
1
1
1
AND
AND
AND
AND
0
0
0
1
0
1
0
1
1
1
1
1
OR
OR
OR
OR
Boolean AND Logic
Boolean OR Logic
Notes: Depending what you are trying to do will depend on which type of Boolean math you will use. Routers route traffic according to Internet Protocol (IP) addresses and the subnet mask associated with each IP address. You will learn routers, routing and IP addressing in detail in the very near future, but for now we will focus on the fundamentals how we use Boolean logic to work with IP addresses and subnet masks.

## Slide 3: IP Management Organizations
Internet Corporation for Assigned Names and Numbers (ICANN)
  Responsible for IP address space allocation
    IPv4 addresses depleted in 2011, ICANN leading the cutover to IPv6
  Domain Name System (DNS) management
  Not for profit
  No ICANN = no global internet
Notes: To reach another person on the Internet you have to type an address into your computer - a name or a number. That address has to be unique so computers know where to find each other. ICANN coordinates these unique identifiers across the world. Without that coordination we wouldn't have one global Internet.
ICANN was formed in 1998. It is a not-for-profit partnership of people from all over the world dedicated to keeping the Internet secure, stable and interoperable. It promotes competition and develops policy on the Internet’s unique identifiers.
ICANN doesn’t control content on the Internet. It cannot stop spam and it doesn’t deal with access to the Internet. But through its coordination role of the Internet’s naming system, it does have an important impact on the expansion and evolution of the Internet.
What is the domain name system?
The domain name system, or DNS, is a system designed to make the Internet accessible to human beings. The main way computers that make up the Internet find one another is through a series of numbers, with each number (called an “IP address”) correlating to a different device. However it is difficult for the human mind to remember long lists of numbers so the DNS uses letters rather than numbers, and then links a precise series of letters with a precise series of numbers.
(for more information see: https://www.icann.org/)

## Slide 4: IP Management Organizations
Internet Assigned Numbers Authority (IANA)
  Operated by ICANN
  Coordinates daily key elements for Internet
  Allocated IP addresses to 5 Regional Internet Registries (RIR)
    APNIC (Asia/Pacific)
    ARIN (North America)
    RIPE NCC (Europe, Middle East, Central Asia)
    LACNIC (Latin America and Caribbean)
    AfriNIC (Africa and Indian Ocean)
Notes: IANA is responsible for coordinating some of the key elements that keep the Internet running smoothly. While the Internet is renowned for being a worldwide network free from central coordination, there is a technical need for some key parts of the Internet to be globally coordinated, and this coordination role is undertaken by IANA.
Specifically, they allocate and maintain unique codes and numbering systems that are used in the technical standards (“protocols”) that drive the Internet.
The various activities can be broadly grouped in to three categories:
Domain Names Management of the DNS Root, the .int and .arpa domains, and an IDN practices resource.
Number Resources Co-ordination of the global pool of IP and AS numbers, primarily providing them to Regional Internet Registries (RIR).
Protocol Assignments Internet protocols’ numbering systems are managed in conjunction with standards bodies.
They are one of the Internet's oldest institutions, with the IANA functions dating back to the 1970s. Today the services are provided by Public Technical Identifiers, a purpose-built organization for providing the IANA functions to the community. PTI is an affiliate of ICANN, an internationally-organized non-profit organization set up by the Internet community to coordinate our areas of responsibilities.
(for more information see: http://www.iana.org/)

## Slide 5: IP Management Organizations
ICANN, IANA & RIR relationship
  ICANN has the strategic view
  IANA has the daily operations
  RIR manages their region
ICANN
IANA
APIC
ARIN
RIPE NCC
LACNIC
AfriNIC
Notes: Internet Corporation for Assigned Names and Numbers (ICANN) oversees the overall operation of the internet. It is the strategic portion of the internet and has delegated authority to Internet Assigned Numbers Authority (IANA).
IANA oversees the daily operations and manages the tactical operation of the internet. It has five Regional Internet Registries (RIR).
RIRs control the operations within their assigned region.
ANALOGY: Your ISP buys a large block of IP addresses from ARIN (North America), who got a larger block from IANA. They then sell you internet service, part of which typically includes a single world-routable (public-facing) IP address
STORIES/RELATE-TO-JOB: The DoD had to go to IANA to request a block of IP addresses for Military networks & systems. You can go to ARIN’s webpage or use a third-party lookup site (like www.dnsstuff.org, or www.whatismyipaddress.com) to find out where an IP address is coming from (which country or RIR). When AFCERT does an investigation into suspicious traffic they can track down the country of origin using IANA’s databases.
When Capt Ketchum’s firewall starting sending him alerts that someone was trying to break into his network, the alert had the attacker’s IP address. By looking-up that address in ARIN’s database he found that it was coming from a block of addresses that was given to APNIC. APNIC’s site revealed that the IP was sold to China’s UNICOM ISP. That doesn’t mean necessarily that the attacker is Chinese, but whoever is attacking his network is coming through China as their last stop before attacking his network.

## Slide 6: IP Addressing
Internet Protocol (IP) Addressing
  Need to identify devices connected to a network
  Based on a logical numbering scheme
  IPv4 based on 32 bits and is most common
    Uses the binary numbering system
  IPv6 based on 128 bits and becoming more common
    Uses the hexadecimal numbering system
Notes: This slide is the basic overview of IP addressing. IP addressing is required to connect to other devices, especially true when they are not on your Local Area Network (LAN). IP addresses are required to leave your LAN and connect to a different LAN. IP addresses are based on a logically based numbering system; the address can be changed based on the network you are currently connected to. We will take a deep dive into IPv4 since it is the most common. IPv6 will some day replace IPv4, so we will look at some facts based on IPv6 after the deep dive into IPv4. Interesting note: IANA gave out last block of IPv4 addresses in February 2011.
What is an IP Address?
All the computers of the world in the Internet network communicate with each other with underground or underwater cables or wirelessly. If I want to download a file from the internet or load a web page or literally do anything related to the internet, my computer must have an address so that other computers can find and locate mine in order to deliver that particular file or webpage that I am requesting. In technical terms, that address is called IP Address or Internet Protocol Address.
Let us understand it with another example; if someone wants to send you a letter, then he/she must have your home address. Similarly, your computer also needs an address so that other computers on the internet can communicate with each other without the confusion of delivering information to someone else’s computer. And that is why each computer in this world has a unique IP Address. Or in other words, an IP address is a unique address that is used to identify computers or nodes on the internet. This address is just a string of numbers written in a certain format. It is generally expressed in the set of numbers for example 192.155.12.1. Here each number in the set is from 0 to 255 range. Or we can say that a full IP address ranges from 0.0.0.0 to 255.255.255.255. And these IP addresses are assign by IANA(known as Internet Corporation For Internet Assigned Numbers Authority).
Working of IP addresses:
The working of IP addresses is similar to other languages. It can also use some set of rules to send information. Using these protocols we can easily send, receive data or files to the connected devices. There are several steps behind the scenes. Let us look at them
- Your device directly requests your Internet Service Provider which then grants your device access to the web.
- And an IP Address is assigned to your device from the given range available.
- Your internet activity goes through your service provider, and that they route it back to you, using your IP address.
- Your IP address can change. For example, turning your router on or off can change your IP Address.
- When you are out from your home location your home IP address doesn’t accompany you. It changes as you change the network of your device.
Types of IP Address
IP Address is of two types:
1. IPv4: Internet Protocol version 4. It consists of 4 numbers separated by the dots. Each number can be from 0-255 in decimal numbers. But computers do not understand decimal numbers, they instead change them to binary numbers which are only 0 and 1. Therefore, in binary, this (0-255) range can be written as (00000000 – 11111111). Since each number N can be represented by a group of 8 digit binary digits. So, a whole IPv4 binary address can be represented by 32-bits of binary digits. In IPv4, a unique sequence of bits is assigned to a computer, so a total of (2^32) devices approximately = 4,294,967,296 can be assigned with IPv4.
IPv4 can be written as: 189.123.123.90
Classes of IPv4 Address: There are around 4.3 billion IPv4 addresses and managing all those addresses without any scheme is next to impossible. Let’s understand it with a simple example. If you have to find a word from a language dictionary, how long will you take? Usually, you will take less than 5 minutes to find that word. You are able to do this because words in the dictionary are organized in alphabetical order. If you have to find out the same word from a dictionary that doesn’t use any sequence or order to organize the words, it will take an eternity to find the word. If a dictionary with one billion words without order can be so disastrous, then you can imagine the pain behind finding an address from 4.3 billion addresses. For easier management and assignment IP addresses are organized in numeric order and divided into the following 5 classes :
- Class A 0-127
- Class B 128-191
- Class C 192-223
- Class D 224-239
- Class E 240-254
2. IPv6: But, there is a problem with the IPv4 address. With IPv4, we can connect only the above number of 4 billion devices uniquely, and apparently, there are much more devices in the world to be connected to the internet. So, gradually we are making our way to IPv6 Address which is a 128-bit IP address. In human-friendly form, IPv6 is written as a group of 8 hexadecimal numbers separated with colons(:). But in the computer-friendly form, it can be written as 128 bits of 0s and 1s. Since, a unique sequence of binary digits is given to computers, smartphones, and other devices to be connected to the internet. So, via IPv6 a total of (2^128) devices can be assigned with unique addresses which are actually more than enough for upcoming future generations.
IPv6 can be written as: 2011:0bd9:75c5:0000:0000:6b3e:0170:8394
Source: https://www.geeksforgeeks.org/what-is-an-ip-address/

## Slide 7: IPv4 Structure
The IPv4 address
  IP version 4 address consists of 32 bits
  Grouped into 4 bytes or “octets”
  We use dotted decimal notation to represent IP addresses
10101000.11000111.01000100.10001001
168 . 199 . 68 . 137
Notes: Currently, IPv4 is by far the most common IP addressing scheme. It is based on a 32 bit address. The address consists of 4 bytes, aka octets. We group the address together using dotted decimal notation; the devices do not need the dots between the octets, but people do! (Imagine the dots not being present when reading the binary 1s and 0s.) Even with the dots separating the octets, it is still difficult to read this address. Because people find binary difficult to read, we use the dotted decimal notation, or we use regular numbers such as 168.199.68.137 for writing addresses.

## Slide 8: IPv4 Logic
IPv4 addresses are logical addresses
  IP addresses are assigned by a LAN administrator
  Host addresses are based on the network it is connected to
Logical numbering scheme – there is
An explanation to the number assigned.
Example: if you dial 662-867-5309 you will
call someone in this area.
If you dial 228-867-5309 you will
call someone in this area.
Notes: Because IP addresses are logical, the addresses must have logical groupings. A LAN technician will assign a LAN an IP address and all the devices on that LAN will share a portion of that LAN IP address. Routers separate LANs, therefore, devices on a LAN must share a common network IP address. Devices may not have an IP address that is not a part of the network it is connected to. Because the IP address is logical, the network (and all connected devices) are assigned an IP address by a LAN administrator.
When you connect a computer to a network, the IP address must have an IP address that is based on the network it is connected to. When you take your computer to another location (and to a different network) the computer will need a new IP address. This time the IP must be an IP based on the new network. The IP address is logical and will change every time you connect to a different network.

## Slide 9: Network and Host Addressing
IPv4 addresses are divided into a network portion and host portion
  Network portion help to identify routes through a network cloud
  Host portion are for devices connected to a particular network
  Different networks must be separated by routers
Router
222.111.33.122
222.111.33.52
221.222.44.37
Switch
Router
Router
Router
Router
Switch
Network
222.111.33.0
Network
221.222.44.0
Notes: Because IP addresses are logical, the addresses must have logical groupings. A LAN technician will assign a LAN an IP address and all the devices on that LAN will share a portion of that LAN IP address. Routers separate LANs, therefore, devices on a LAN must share a common network IP address. Devices may not have an IP address that is not a part of the network it is connected to. Because the IP address is logical, the network (and all connected devices) are assigned an IP address by a LAN administrator.
When you connect a computer to a network, the IP address must have an IP address that is based on the network it is connected to. When you take your computer to another location (and to a different network) the computer will need a new IP address. This time the IP must be an IP based on the new network. The IP address is logical and will change every time you connect to a different network.
In the diagram, when a device in network 222.111.33.0 needs to send information to a device in network 221.222.44.0, the source work station will need to know the IP address of the distant end work station before it is able to send any data. The source address and the destination address is assigned to a packet of information. As the router receives the packet, the addresses are read and then sent to a neighboring router to get the packet to the distant end network 221.222.44.0 and the last router connected will place the packet onto the network where it will it find its destination work station. The distant end work station will know who to reply to since the source address is in the packet along with the information sent to it. Because an IP address has both network and host information, each packet of information can be routed from one destination to another and across a multitude of networks.

## Slide 10: IPv6
IPv6 is the new IP addressing convention
  Replacing IPv4 because there are no more IPv4 addresses
    IPv4 provides over 4 billion addresses
    IPv6 provides over 340 trillion trillion trillion addresses
  IPv6 characteristics
    128 bits for addressing
    Hexadecimal notation
    Notation can be abbreviated
Notes: In 1980 when the internet consisted of about 600 computers. A 32 bit address creating over 4 billion IP addresses seemed to be more than enough. In 1990 the internet was introduced to the commerce (.com) world and the internet grew exponentially, so much growth has happened since then; we are nearly out of addresses to place on devices. The reason for creating CIDR, VLSM and Network Address Translation (NAT) was to extended the life of IPv4 addressing. The biggest fix to the depletion of IPv4 addresses was the creation of IPv6. IANA gave out last block of IPv4 addresses in February 2011.
IPv6 is a new standard of IP addressing. It is based on a 128 bit address and gives us many more address than what IPv4 ever could – IPv6 provides about 32 addresses per square inch of dry land on the earth. Besides creating substantially more addresses, it has changed from dotted decimal notation used by IPv4 to eight groups of 4 hexadecimal notation. With groups of 4 hex characters, with IPv6 we refer to the address as having “quartets” instead of octets. The new hex format can also be abbreviated. There are also several more improvements with implementing IPv6.
What is IPv6?
IPv6 is a new version of the Internet Protocol that will eventually replace IPv4, the version that is most widely used on the Internet today. IPv6 is a well established protocol that is seeing growing usage and deployment, particularly in mobile phone markets.
How does IPv6 solve the problem of IPv4 address exhaustion?
IPv6 uses 128-bit addresses as opposed to the 32-bit addresses used by IPv4, allowing for a substantially larger number of possible addresses. With each bit corresponding to a ‘0’ or ‘1’, this theoretically allows 2^128 combinations or 340 trillion, trillion, trillion addresses. By contrast, IPv4 permits 2^32 combinations for a maximum of approximately 4.7 billion addresses.
n practice, the actual number of usable addresses is slightly less as IPv6 addresses are structured for routing and other purposes, whilst certain ranges are reserved for special use. The number of IPv6 addresses available, though, is still extremely large.
Network operators and large enterprises are typically expected to be assigned a /32 address block, smaller enterprises a /48, and home users a /56 (when they would typically get a single IPv4 address). This allows for scalability and future subnetting, and a virtually-unlimited number of addresses in each /64 subnet.
There is an erroneous perception that the assignment of large IPv6 prefixes to end customers is wasteful, but the IPv6 address space is so huge that it has been calculated (by Tony Hain) that a /48 could be assigned to every human for the next 480 years before they run out.
Security
It has been said that IPv6 supports improved security because the IP Security (IPsec) was originally developed for IPv6 and it implementation was intended to be a mandatory part of the protocol. However, IPsec can also be used with IPv4, and is now simply recommended for use with IPv6 because it was considered impractical to require full IPsec implementations for all types of devices that may use IPv6. The benefits of using IPsec are similar with both IPv4 and IPv6.
Source: CCNA ICND1 100-105 pages 661-676
https://www.internetsociety.org/deploy360/ipv6/faq/

## Slide 11: IPv6 Notation
Notation is based on eight groups of four hex characters “quartets”
  Example: fe00:0000:0000:0001:0000:0000:0000:0056
  Not case sensitive
  Abbreviate by removing leading 0s in a quartet
    Example: fe00:0:0:1:0:0:0:56
  Abbreviate by replacing two or more consecutive “0” quartets with “::”
    Example: fe00:0:0:1::56
    Note: when there are more than one group of consecutive 0s, replace the longest sequence with “::”
Notes: IPv6 notation is based on eight groups of four hex characters known as “quartets.” The characters are not case sensitive and IPv6 notation can be abbreviated using two simple rules based on 0s.
IPv6 addresses are written using hexadecimal, as opposed to dotted decimal in IPv4. Because an hexadecimal number uses 4 bits this means that an IPv6 address consists of 32 hexadecimal numbers. These numbers are grouped in 4’s giving 8 groups or blocks. The groups are written with a : (colon) as a separator.
group1:group2: ……etc…. :group8
Source: CCNA ICND1 100-105 pages 661-676 )
http://www.steves-internet-guide.com/ipv6-guide/

## Slide 12: IPv6 Characteristics
Network bits and host bits
  IPv6 uses a “prefix” to identify network bits with “/#”
    The “#” is any number between 0 and 128
    Designates which part of the address is for the network
    2001:0db8:aaaa:0002:1234:5678:9abc:ef01/64
    2001:0db8:aaaa:0002:1234:5678:9abc:ef01
Prefix bits
Host bits
Notes: IPv6 notation has a CIDR type of notation to identify the deference between the network and the host portions of the address.
Network And Node Addresses
In IPv4 an address is split into two components a network component and a node component.
This was done initially using address classes and later using subnet masking.
In IPv6 we do the same. The first step is to split the address into two parts.
The address is split into 2 64 bit segments the first 64 bits is the network part and the second 64 bits the node part:
First 64 bit segment (Network) + second 64 bit segment (Node) = 128 bits total.
The first 64 bits are used for routing.
The second 64 bits identify the address of the interface or node, and is derived from the actual physical or MAC address using IEEE’s Extended Unique Identifier (EUI-64) format.
If we look at the first 64 bits in more detail we can see that it is split into 2 blocks of 48 and 16 bits respectively the lower 16 bits are used for subnets on an internal networks, and are controlled by a network administrator. The upper 48 bits are used for the global network addresses and are for routing over the internet.
First 64 bit segment (Network) = 48 bits (Global Unicast Address) + 16 bits (subnet ID)
Source: CCNA ICND1 100-105 pages 661-676 for more information on IPv6 see pages 679 - 693)
http://www.steves-internet-guide.com/ipv6-guide/

## Slide 13: IPv4 Vs. IPv6
IPv4 IPv6
32 bit address 128 bit address
4,294,967,296 addresses 340,282,366,920,938,463,463,374,607,431,
768,211,456 addresses
Binary Hexadecimal
Assigned to host Host auto configure
No security Integrated security
Cannot abbreviate Can abbreviate
Requires subnet Use /P (prefix bits)
Notes: IPv6 has many advantages over IPv4. IPv4 has served us well and we probably would not need to change it…….if only there were enough IPv4 address to keep us going.
(see CCNA ICND1 100-105 pages 661-676)

## Slide 14: Classful IP Addressing
There are five classes of IPv4 IP addresses
  Class A Used for internet hosts
  Class B Used for internet hosts
  Class C Used for internet hosts
  Class D Used for internet multicasts
  Class E Unused—used experimentally
  We will focus on Class A, B and C addresses
Notes: There are 5 classes of IP addresses. We will only study class A, B and C because they are the only classes that can support host devices on a network.

## Slide 15: Classful IP Addressing
Determining the class
            Binary must begin with
  Class A First octet is between 0-127 00000000 - 01111111.
  Class B First octet is between 128-191 10000000 - 10111111.
  Class C First octet is between 192-223 11000000 - 11011111.
128
27
X
64
26
X
32
25
X
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
Notes: The IP address class is determined by the first octet.
- If the first octet falls between 0 and 127, it will be a class A address.
- If the first octet has a decimal number between 128 and 191, that address will be a class B address.
- If the first octet is between 192 and 223, it will be a class C address.
This information never changes and you should be able to easily recall this information.

## Slide 16: Private IP Addressing
Private IP addresses
  Not used on public networks
  One range per IP address class
Class
1st Octet
Private IP Addresses
A
0 - 127
10.0.0.0 – 10.255.255.255
B
128 - 191
172.16.0.0 – 172.31.255.255
C
192 - 223
192.168.25.0 – 192.168.25.255
Notes: Private IP addresses are for private networks only. There is a range of IP addresses available for each class. Because these IP addresses are for private use only, these IP addresses will not be used on public networks.

## Slide 17: Special Purpose IP Addressing
Special purpose addresses
  Loopback IP: 127.0.0.1
    Used for testing your computer
  APIPA: 169.254.0.0/16
    Automatic Private IP Address
    Allows device communication
    when no DHCP server exists
Notes: Special purpose IP addresses include loopback 127.0.0.1 and will loop a computer back to itself. The APIPA IP address allows a PC to get on a network when there is no DHCP server available.
What Is 127.0.0.1?
127.0.0.1 is known as a loopback address, but you may see it under the name "localhost." When you point your browser to 127.0.0.1, it tries to connect to the computer you're using right now. This is handy when you want to connect to a server on your own computer.
127.0.0.1 is special among IP addresses. Typically, an IP address is unique to every computer on both your local network and the internet. 127.0.0.1, however, always points to the computer you're currently using no matter what.
APIPA stands for Automatic Private IP Addressing (APIPA). It is a feature or characteristic in operating systems (eg. Windows) which enables computers to self-configure an IP address and subnet mask automatically when their DHCP(Dynamic Host Configuration Protocol) server isn’t reachable. The IP address range for APIPA is (169.254.0.1 to 169.254.255.254) having 65, 534 usable IP addresses, with the subnet mask of 255.255.0.0.
Source: https://www.makeuseof.com/tag/what-is-127-0-0-1-localhost-loopback-address/
https://www.geeksforgeeks.org/what-is-apipa-automatic-private-ip-addressing/

## Slide 18: Classful IP Addressing
Classful IP addresses have predetermined networks and hosts
  Network portion: assigned by the ICANN
  Host portion: assigned by network administrator
  1
Class A
Network
Host
Host
Host
Class B
Network
Host
Host
Network
Class C
Network
Host
Network
Network
Number of Hosts
Number of Networks
128
16,384
2,097,152
16,777,214
65,534
254
1st Octet
2nd Octet
3rd Octet
4th Octet
Notes: Classful IP address were determined how many networks would be available to a customer. The amount of network are determined by how many octets are used. A class A address uses the first octet to create network, since one octet is 8 bits, we can have 126 networks with a class A address. The remaining three octets are available for hosts. Based on 24 bits in the remaining three octets, there is a possibility of 16,277,214 host per network using a class A address.
A class B address uses two octets to create networks, so a total of 16,384 networks are available. The remaining two octets are available for host addresses; 65,534 hosts are available for each class B network.
Class C addresses uses three octets to create networks. There is 2,097,152 networks available and the last octet is used for host addresses; 254 hosts per network is available.
History of classful addressing
Prior to classful addressing, the first eight bits of an IP address defined the network a given host was a part of. This would have had the effect of limiting the internet to just 254 networks. Each of those networks contained 16,777,216 different IP addresses. As the internet grew, the inefficiency of allocating IP addresses this way became a problem. After all, there are a lot more than 254 organizations that need IP addresses, and a lot fewer networks that need 16.7 million IP addresses to themselves.
Simply put: we needed a way to more efficiently allocate addresses. In 1981, RFC791 and classful addressing came along to help solve that problem. With classful addresses, we went from just 254 available networks to 2,113,664 available networks. How?
How classful addressing works
Classful addressing divides the IPv4 address space (0.0.0.0-255.255.255.255) into 5 classes: A, B, C, D, and E. However, only A, B, and C are used for network hosts. Class D, which covers the 224.0.0.0-239.255.255.255 IP address range, is reserved for multicasting, and class E (240.0.0.0-255.255.255.255) is reserved for “future use.”
What are the limitations of classful IP addressing?
As you can probably guess, the internet is hungry for IP addresses. While classful IP addressing was much more efficient than the older “first 8-bits” method of chopping up the IPv4 address space, it still wasn’t enough to keep up with growth.
As internet popularity continued to surge past 1981, it became clear that allocating blocks of 16,777,216, 65,536, or 256 addresses simply wasn’t sustainable. Addresses were being wasted in too-large blocks, and it was clear there’d be a tipping point where we ran out of IP address space altogether.
One of the best ways to understand why this was a problem is to consider an organization that needed a network just slightly bigger than a Class C. For example, suppose our example organization needs 500 IP addresses. Going up to a Class B network means wasting 65,034 addresses (65,534 usable Class B host addresses minus 500). Similarly, if it needed just 2 public IP addresses, a Class C would waste 252 (254 usable addresses – 2).
Any way you look at it, IP addresses under the IPv4 protocol were running out, either through waste or the upper limits of the system.
Fact: There’s a calculated limit of 4,294,967,296 IPv4 addresses, and they were exhausted on April 21, 2017.
Source: https://www.auvik.com/franklyit/blog/classful-classless-addressing/
https://www.tutorialspoint.com/ipv4/ipv4_address_classes.htm

## Slide 19: Classful IP Addressing
Identify the class and how many octets are used for the network
  199.46.36.5
  111.211.11.1
  177.141.30.89
  22.8.56.107
  192.168.16.2
  163.100.5.1
Notes: Class A 0-127
Class B 128-191
Class C 192-223

## Slide 20: Classful IP Addressing
Identify the class and how many octets are used for the network
  199.46.36.5 Class C
  111.211.11.1 Class A
  177.141.30.89 Class B
  22.8.56.107 Class A
  192.168.16.2 Class C
  163.100.5.1 Class B
Notes: Class A 0-127
Class B 128-191
Class C 192-223

## Slide 21: IP Addressing
Network ID
  Host on a network must identify with the network it is connected to
  Network ID is an IP address used only to identify the network
    Network ID is the first IP address in a range of IP addresses
    Network ID cannot be assigned to any device
    All zeros in the host portion of the address
200.23.45.0
200.23.45.1
200.23.45.254
200.23.45.255
The first IP in a range of
IP addresses will be the network ID
Notes: All networks must have an identifier and the identifier comes in the form of an IP address.
The network number, also called the network ID or network address, identifies the network. By definition, the network number is the numerically lowest number in the network. However, to prevent any ambiguity, the people that made up IP addressing added restriction that the network number cannot be assigned as an IP address. So, the lowest number in the network is the network ID. Then, the first (numerically lowest) host IP address is one larger than the network number.
Source: ICND1 100-105 pages 326-327

## Slide 22: IP Addressing
Broadcast Address
  Used to message all network devices on the specific network ID
    Broadcast IP is the last IP address in a range of IP addresses
    Broadcast IP cannot be assigned to any device
    All ones in the host portion of the address
200.23.45.0
200.23.45.1
200.23.45.254
200.23.45.255
The last IP in a range of IP addresses
will be the broadcast IP
Notes: Each device in a network must be able to broadcast to all other devices connected to the same network. The broadcast address is designated to be all ones in the host portion of the address.
Imagine you’re Paul Revere, riding from Boston to Lexington to warn citizens that the redcoats were coming. He may not be as fast as computer networks today, but Paul Revere was essentially acting much like a broadcast would- he was relaying his message to the entire town of Lexington.
A broadcast, in particular, is a simple message that is sent to all clients on a local area network. But just exactly what enables a network to broadcast a message to every single client on the network?
WHAT IS A BROADCAST ADDRESS?
A broadcast address is an address used to indicate that information being sent out should be delivered to every client on the local area network. These addresses are always the highest number possible in a particular network address or subnet.
Source: ICND1 100-105 pages 327, 478-479
https://www.itprc.com/how-a-broadcast-address-works/

## Slide 23: Subnet Mask
Subnet mask corresponds to each IP address
  Similar to IP addresses, we use the dotted decimal numbering system
  Based on the binary numbering system
    A binary 1 in the subnet mask designates a network bit
    A binary 0 in the subnet mask designates a host bit
10101001
169.
01000101
69.
10001001
137
11000111
199.
11111111
255.
00000000
0
11111111
255.
00000000
0.
Network
Host
Host
Network
IP Address
Subnet Mask
Notes: The subnet mask, like the IP address itself is a 32 bit number and based on the binary numbering system and is a dotted decimal number. Unlike the IP address binary numbers, where the 1s are determined by the dotted decimal number it represents, the subnet mask 1s determine the dotted decimal number. Hence, a binary 1 will always be a network bit and a 0 will always be a host bit. Also, network bits will always be consecutive, counting from the left and the remaining non-network bits will be 0s for the remainder of the subnet mask.
A subnet mask is a number that distinguishes the network address and the host address within an IP address. A subnet is a smaller network within a network that requires a subnet mask.
Subnetting is the process of dividing a network into two or more subnets. Its primary function is to make the routing of data within a network more efficient and secure. Subnetting also helps make better use of IPv4 addresses.
When you connect a device to a network, the network assigns an IP address to the device. That IP address consists of two parts: the network portion and the host portion. The network portion of the IP address identifies the overall network while the host portion identifies the device.
The network address and host address contained in an IP address are indistinguishable from each other without a subnet mask. The subnet mask allows network traffic to understand IP addresses by splitting them into the network and host addresses.
Source: https://www.ipxo.com/blog/what-is-subnet-mask/

## Slide 24: Subnet Mask
First two octets refer to the network portion of this class B address
Second two octets refer to the host portion of this class B address
  Note: all the 1 bits are network bits, all the 0s are host bits
10101001
169.
01000101
69.
10001001
137
11000111
199.
11111111
255.
00000000
0
11111111
255.
00000000
0.
Network
Host
Host
Network
IP Address
Subnet Mask
Notes: Note the subnet mask is all 1s in the network portion and then all 0s in the host portion. Unlike the IP address, the subnet mask will always have the 1s together in a row, followed by the host bits (0s) all in a continuous row.

## Slide 25: Subnet Mask
Default subnet masks
11111111
255.
00000000
0.
00000000
0
00000000
0.
11111111
255.
00000000
0
11111111
255.
00000000
0.
11111111
255.
00000000
0
11111111
255.
11111111
255.
Class A or /8
Class B or /16
Class C or /24
Notes: The “/” in this slide represents Classless Interdomain Routing (CIDR). CIDR is a very simple way to express how many network bits the subnet mask is using. In this slide, a class A subnet mask has 8 bits for network bits (1s), a class B has 16 network bits and a class C has 24 network bits.

## Slide 26: Subnetting
Convert host bits in a Classful network to be used as network bits
  Subnetting allows an administrator to create more networks
  Creates more (smaller) networks, each network has a range of IP addresses
  Classless addresses are created when subnetting a Classful network
Network
Host
Network
Subnet
Notes: Subnetting allows an administrator to create more networks than what a Classful address naturally provides. This is done when the administrator converts a host bit into be a network bit. Host bits can be changed into network bits but network bits cannot be changed into host bits. When an administrator subnets an IP address, more networks are created at the cost of hosts—there will be two less hosts available for each network. Also, when the administrator subnets an address, the Classful address is now a classless address.
Why use subnetting?
Subnetting serves a number of purposes. From giving administrators more control over their networks and improving their networks’ performance. To boosting security and making more efficient use of IP addresses. Here are some of the key benefits.
More efficient routing of data
Broadcast traffic creates a big inefficiency in networks. This traffic involves data packets traversing the network to every node. By dividing broadcast domains, subnetting reduces the number of nodes that broadcast traffic interacts with and makes the routing of data packets more direct and efficient.
You can think of a subnet as allowing different devices to communicate with different smaller networks, rather than all trying to communicate with the same network at the same time.
Let’s take 100 people trying to talk at the same time in a Zoom call as an example. There’d be too much information and noise to take anything in. However, if those 100 people split into 20 breakout rooms, they could have much more peaceful and productive conversations.
Subnet masks are key here. That’s because a subnet mask is what makes sure that traffic stays contained within its designated subnet. This reduces major congestion and the load imparted on the network.
Subnetting effectively decreases the distance that data packets need to travel in the network. This also allows the network to route data more efficiently.
All of this increases the speed and overall performance of the network.
Better network security
If you’re operating a large local network, with many connected devices and a high volume of network traffic, there are a number of security advantages of running multiple subnets rather than one larger network.
Most notably, if a subnet is compromised by an attack, only that network segment will be affected. Using subnets, instead of all devices on the same network being visible to attackers, they would only have access to other devices on the same subnet.
You may want to create subnets to keep legitimate local network traffic siloed, too. Subnets make it possible to prevent all devices from accessing the entire network. This is a great solution if you want to keep certain files or processes secure or limit remote network access.
Increased lifespan of IPv4
When the internet was first coming into use, it was easy to get an IP address. Since there is a limited number of possible IPv4 addresses, the available IP address stock quickly began to diminish.
Looking for an IP address solution, creative minds came up with the idea of using subnetting to increase the utility of a single public IP address.
Instead of each device having a unique IP address, a network can have a number of private IP addresses on a single IP network. This means that each device on an IP network has an IP address with a part that refers to the overall network IP address, and a part that refers to its subnet.
This is why IPv4 remained the internet standard for much longer than if subnetting was not an option.
Source: ICND1 100-105 pages 312-313
https://www.ipxo.com/blog/what-is-subnet-mask/

## Slide 27: Subnetting
Subnetting a class B address
16 bits
16 bits
16 bits
8 bits
8 bits
11111111
255.
00000000
0
11111111
255.
11111111
255.
11111111
255.
00000000
0
11111111
255.
00000000
0.
Classful B
Subnet mask
Classless B
Subnet mask
Notes: In this example, a class B address was subnetted. A class B address has 16 host bits to create new subnetwork IDs. The administrator needs more networks so all 8 host bits in the 3rd octet were converted to network bits and this creates an additional 256 networks. Now there are only 254 address available for each of the new 256 networks, whereas in a Classful class B network there was 1 network with 65,534 host available.
Source: ICND1 100-105 pages 312-313

## Slide 28: Subnetting
Subnetting a class B address
  8 bits in subnet field creates 256 subnets (2s = number of subnets)
  8 bits in host field provides 254 hosts (2h – 2 or 2# of host bits – 2)
  Remember: we started with 65,534 hosts with this class B address
16 bits
8 bits
8 bits
11111111
255.
00000000
0
11111111
255.
11111111
255.
Notes: By converting 8 host bits in the 3rd octet, we were able to create 256 subnetworks. Use the formula (2s = number of subnets) to determine how many subnets can be created by converting host bits into network bits. In the example above, we converted 8 host bits into network bits, so 28= 256 subnets. Now there are only 254 address available for each network, whereas in a Classful class B network there were 65,534 host available.
2h – 2 or 2# of host bits – 2 this formula determines the amount of IP addresses available to place onto devices in each subnet. You have to subtract 2 network addresses within each subnet because the first IP address (all 0s in the host bits) will be used for the network ID. The other IP address that is mandatory for each subnet is the Broadcast address (all 1s in the host bits).
Source: ICND1 100-105 pages 312-313

## Slide 29: Subnetting
Creating subnetworks
  How many subnets can you create?
  Use the formula: 2s = # of subnets
    2s: S = subnet bits
    Subnet bit: was host bit (0) but now network bit (1)
2s = # of subnets
21 = 2 subnets
Subnet 1 = .0 - .127
Subnet 2 = .128 - .255
00000000
0
10000000
.128
4th Octet
1
0 127
128 255
128 255
0 127
1 subnetted bit creates two subnets.
Each subnet has 128 IP addresses.
Subnet
Mask
IP
Address
Notes: This slide demonstrates how we manipulate a host bit in our Octet of Interest (OOI). We are converting the class C classful address 207.21.54.0 into two subnetworks. To create two subnets, we need to convert one host bit to make the two subnets. Use the formula 2s = # of subnets (21 = 2 subnets, 22 = 4 subnets, 25 = 32 subnets, etc.,). We created two subnets by converting one host bit to a network bit. The first subnet (subnet #1) has a range of IP addresses between 207.21.54.0 to 207.21.54.127, we have 128 IP addresses in each subnet created. Remember, this octet started out with 256 Ip addresses; we split the octet into two smaller subnets, each with 128 IP addresses each. The second subnet (subnet #2) has the range of IP addresses between 207.21.54.128 to 207.21.54.255.
If a device has an address of 207.21.54.37 it would belong to the first subnet, subnet #1. Conversely, if a device has an address of 207.21.54.137 it would belong to the second subnet, subnet #2.
Source: ICND1 100-105 pages 300-330

## Slide 30: How Many Subnets?
2s = # of subnets
  Determine how many host bits need to be converted to network bits
21 = 2 29 = 512
22 = 4 210 = 1,024
23 = 8 211 = 2,048
24 = 16 212 = 4,096
25 = 32 213 = 8,192
26 = 64 214 = 16,384
27 = 128 215 = 32,768
28 = 256 216 = 65,536
Host
bits
Networks
Host
bits
Networks
Notes: Using the formula 2s = # of subnets; we can determine how many host bits need to be converted to network bits in order to create more networks.

## Slide 31: Subnetting
Hosts per subnetwork
  How many hosts can you have on each subnet?
  Use the formula: 2h-2 = # of hosts per subnet
    2h: H = host bits
    (-2) IP addresses for Subnet ID and Broadcast IP
00000000
0
10000000
.128
4th Octet
1
0 127
128 255
128 255
0 127
2h -2= # of hosts per subnet
27 -2= 128 – 2 = 126 hosts
Subnet 1 = 126 hosts
Subnet 2 = 126 hosts
7 host bits (0’s) in the subnet mask determines
the total number of hosts per subnet.
Subnet
Mask
IP
Address
Notes: Using the formula 2h-2 = # of hosts, we can determine how many hosts will be on each subnet. We subtract two (-2) IP addresses from each subnet we create. We must do this because each subnet must have both a subnet ID and a broadcast IP. Neither IP address cannot be assigned to a host.
Before subnetting, this class C octet had 256 IP addresses (.0 - .255) and two IP addresses were not to be assigned to the hosts. The very first IP address 207.21.54.0 is used as the network ID and the last IP address, 207.21.54.255, is used as the broadcast IP for the network. This leave 254 IP addresses to support individual hosts.
We subnetted one host bit and created two subnets. Each subnet has 128 IP addresses assigned to it. Each subnet must have a subnet ID and a broadcast IP address, therefore, each subnet can support 126 hosts per subnet. The first subnet will have the subnet ID of 207.21.54.0 with the broadcast IP address of 207.21.54.127
The second subnet will have the subnet ID of 207.21.54.128 with the broadcast IP address of 207.21.54.255
Note: We lose two IP addresses for each subnet created.
Source: ICND1 100-105 pages 300-330

## Slide 32: How Many Hosts?
2h = # of hosts - 2
  Create networks large enough to support (X) number of hosts
21 = 2 – 2 = 0 29 = 512 - 2 = 510
22 = 4 – 2 = 2 210 = 1,024 – 2 = 1,022
23 = 8 – 2 = 6 211 = 2,048 – 2 = 2,046
24 = 16 – 2 = 14 212 = 4,096 – 2 = 4,094
25 = 32 – 2 = 30 213 = 8,192 – 2 = 8,190
26 = 64 – 2 = 62 214 = 16,384 – 2 = 16,382
27 = 128 – 2 = 126 215 = 32,768 – 2 = 32,766
28 = 256 – 2 = 254 216 = 65,536 – 2 = 65,534
Host
bits
Hosts
Host
bits
Hosts
Notes: In this slide, (X) is a variable number, (X = 123 hosts; or X = 11,223 hosts)
Similar to the previous exercise (exercise #4), we need to determine how many bits are required to support our requirement. Unlike the previous exercise, we are allocating bits to support the required amount of hosts instead of subnetworks. When we allocate bits to create subnetworks, we count bits from the left. It is the opposite for allocating bits for hosts – we count bits from the right.
Creating (X) number of subnets: convert host bits into network bits by counting from the left. Example: create 8 subnets (23 = 8 subnets) using a B class subnet mask
255 . 255 . 0 . 0
11111111.11111111.11100000.00000000 Note: 3 host bits changed to network bits

To create 8 subnets, take the first three host bits counting from the left to right 
Creating (X) number of hosts per subnet: reserve host bits to insure there are enough host bits to support (X) of hosts on each subnet by counting from the right. Example: insure 6 hosts per subnet (23 = 8 hosts -2) using a B class subnet mask
255 . 255 . 0 . 0
11111111.11111111.11111111.11111000 Note: 3 host bits changed to network bits

To reserves 6 hosts per subnet, count from the right to the left to insure there will be 6 hosts per network. 

## Slide 33: Subnetting
Convert host bits to network bits by changing 0 to 1
  The class B subnet mask 255.255.0.0 becomes 255.255.128.0 when converting a single host bit to a network bit
128
27
1
128
64
26
0
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
Value of binary
place holder
Subnet mask
number
Notes: By converting a single bit to a network bit, the subnet mask changes based on the value of the bit you converted. In this case the value of the bit was 128. When converting host to network bits, we always convert the bits starting from the left of our number chart.
Source: ICND1 100-105 pages 312-313

## Slide 34: Subnetting
Convert host bits to network bits by changing 0 to 1
  The class B subnet mask 255.255.0.0 becomes 255.255.192.0 when converting two host bits to network bits (128 + 64 = 192)
128
27
1
128
64
26
1
192
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
Value of binary
place holder
Subnet mask
number
Notes: By converting two host bits to network bits, the subnet mask changes based on the value of the bits you converted. In this case the value of the first bit was 128 and the value of the second bit is 64. When these two bits are added together we get the value of 192 (128 + 64 = 192)
Source: ICND1 100-105 pages 312-313

## Slide 35: Subnetting
Convert host bits to network bits by changing 0 to 1
  Continue adding the value of the converted bits when creating subnets
  If all bits in an octet is used, the subnet is 255
The 3rd octet of a class B address
128
27
1
128
64
26
1
192
32
25
1
224
16
24
1
240
8
23
1
248
4
22
1
252
2
21
1
254
1
20
1
255
Value of binary
place holder
Subnet mask
number
Notes: By converting host bits to network bits, the subnet mask changes based on the value of the bits you converted. In this case the value of all the bits added together we get the value of 255 (128 + 64 + 32 + 16 + 8 + 4 +2 +1 = 255)
If 1 host bit is converted to a network bit the subnet mask is 128
If 2 host bits are converted to network bits the subnet mask is 192 (128 + 64 = 192)
If 3 host bits are converted to network bits the subnet mask is 224 (128 + 64 + 32 = 224)
If 4 host bits are converted to network bits the subnet mask is 240 (128 + 64 + 32 + 16 = 240)
If 5 host bits are converted to network bits the subnet mask is 248 (128 + 64 + 32 + 16 + 8 = 248)
If 6 host bits are converted to network bits the subnet mask is 252 (128 + 64 + 32 + 16 + 8 + 4 = 252)
If 7 host bits are converted to network bits the subnet mask is 254 (128 + 64 + 32 + 16 + 8 + 4 + 2 = 254)
If 8 host bits are converted to network bits the subnet mask is 255 (128 + 64 + 32 + 16 + 8 + 4 + 2 + 1 = 255)

## Slide 36: Subnetting
You can convert host bits into network bits from multiple octets
  55.0.0.0 255.255.255.224 is a class A address that is using all eight bits from the second and third octets plus three bits from the fourth octet
The 4th octet of a class A address
128
27
1
128
64
26
1
192
32
25
1
224
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
Value of binary
place holder
Subnet mask
number
Notes: You are not limited to just the next octet! As long as there are host bits to convert to network bits, you can use them to make more networks. In this slide, we are using the class A IP address 55.0.0.0 with the subnet mask 255.255.255.224. We know this is a class A IP address because the first octet falls between 0-127. All class A subnet masks are automatically 255.0.0.0 When we see the subnet mask 255.255.255.124 we can determine that all the bits in the second and third octets were used at network bits because they have the value of 255 assigned to them. Because the 4th octet has 224, we can determine that only three bits were converted from host to network bits in the 4th octet.

## Slide 37: Subnetting
How many IP addresses per subnet bit?
  Magic Number: Groups of IP addresses come with each subnet mask
  Look at the binary value of
  the last subnet bit
128
27
1
128
64
26
0
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
128
27
1
128
64
26
1
192
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
128 IP addresses are
Available with a
128 subnet mask
64 IP addresses are
Available with a
192 subnet mask
Notes: With every subnet mask, you will get a certain amount of IP addresses associated with it. In this example we converted one host bit into a network bit and by looking at the binary place holder value, we see that we will get 128 IP addresses to place on our new subnet.
Also, we converted two host bits into network bits. When we look at the binary place holder value of the last network bit, we see a value of 64. When we convert two host bits into network bits, we get a subnet mask of 192 (128 + 64 = 192) and we will get 64 IP addresses for each subnet.
Using the binary place holder value of the subnet bit to calculate the answers to IP questions is often referred to as the “magic number” a.k.a. “rotator number.”
You can also determine the magic number by subtracting the subnet mask that has the last network bit from 256. NOTE: 256 = the number of possible IP addresses (.0 through .255)
Example for last subnet mask (128): 256 Example for last subnet mask (192): 256
Subnet mask: - 128 Subnet mask: - 192
Magic number: 128 Magic number: 64

## Slide 38: Subnetting
How many subnets per subnet bit?
  Imagine there is a box of 256 IP addresses for each octet (0-255)
  Every subnet bit cuts the box(es) in half
0 127
128 255
0 255
128 255
0 127
0
63
64
127
128
191
192
255
0 subnet bit
One group of
256 addresses
1 subnet bit
Two groups of
128 addresses
2 subnet bits
Four groups of
64 addresses
3 subnet bits
Eight groups of
32 addresses
0--31
224--255
Notes: This slide demonstrates how the binary value of the subnet bit is equivalent to how many IP addresses are available based on how many subnet bits are used. When there are no subnets created, there are 256 IP addresses available to use. If we convert the first host bit into a subnet bit, we now have two subnetworks, each network has 128 IP addresses. If we convert another host bit into a subnet bit, we will have created four subnets and each subnet will have 64 IP addresses within each subnet.
Notice how each time we convert a host bit into subnet bits, we get twice as many subnetworks and half as many IP addresses within each subnet.

## Slide 39: Octet Of Interest (OOI)
Octet of Interest (OOI)
  The octet you work in when working with subnets
  Where the last network bit is located in the subnet mask
    More often than not, there will be a mix of 1’s and 0’s
10101001
169
01000101
.69
00000000
0
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
Network
Subnet
Octet of
Interest
Network
IP Address
Subnet Mask
11
Last network bit
Notes: Octet of Interest (OOI) is identified by finding the last network bit (a binary 1) in the subnet mask. If the subnet mask has both binary 1’s and 0’s in it; it will be the octet of interest. The OOI is really the only place where you are required to work in to determine the subnet ID.
If all eight of the host bits in the subnet mask are converted into network bits (all binary one’s), the Boolean AND math will keep the subnet number the same as the IP address number.
In the slide above, note that the first three octets in the IP address is 169.199.69 and after adding the subnet mask to the IP address using Boolean AND; it will remain 169.199.69
IP address: 10101001.11000111.01000101.00000000
Subnet Mask: 11111111.11111111.11111111.11000000
10101001.11000111.01000101.00000000

## Slide 40: Subnet Mask
Using Boolean AND math to determine the subnet ID
  Add the binary IP address to the binary subnet mask
Boolean AND
0 and 0 = 0
0 and 1 = 0
1 and 0 = 0
1 and 1 = 1
Address 1 0 1 0 1 0 0 1 . 1 1 0 0 0 1 1 1 . 1 0 1 0 1 0 0 1. 1 0 0 0 1 0 0 1
Mask 1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 1 0 0 0 0 0 0 0 . 0 0 0 0 0 0 0 0
1 0 1 0 1 0 0 1 . 1 1 0 0 0 1 1 1 . 1 0 0 0 0 0 0 0 . 0 0 0 0 0 0 0 0
Network ID 169 . 199 . 128 . 0
10101001
169.
10101001
169.
10001001
137
11000111
199.
11111111
255
00000000
0
11111111
.255
10000000
.128
IP Address
Subnet Mask
1
Notes: Using Boolean AND algebra you can determine the network ID. Because of the “AND” rules, anytime there is a “255” in the subnet mask, the value will automatically become the value of the IP address the mask corresponds to.

## Slide 41: Subnetting Exercise 3
Complete exercise #3
  First determine the IP address class
  Determine how many bits are used for subnetting
  Determine the subnet the given host IP address belongs to
Notes: Binary math method using 1.) 188.26.221.100 255.255.255.240 from Exercise 3 for example.
1. Determine the class (A = 0-127; B = 128-191; C = 192-223) by looking at the first octet. Look at the following IP address: 188.26.221.100; this IP is a class B address because the first octet is 188 (it is in the range of 128-191). Because it is a class B address, the first two octets are dedicated to network bits (255.255.0.0).
2. Determine the bits for the subnet.
255.255.255.240 = is a class B address (class B = 255.255.0.0). Look at the remaining bits used in the subnet octets. In this case, we are using 8 bits from the third octet (255) and four bits from the fourth octet (240), a total of 12 bits. See below: we are using 12 bits as counted from the left.
3rd Octet 4th Octet
128 192 224 240 248 252 254 255 128 192 224 240 248 252 254 255
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0  1 = network bit
0 = host bit
3. Determine subnetwork ID by using Boolean math
(0 and 0 = 0; 0 and 1 = 0; 1 and 0 = 0; 1 and 1 = 1).
188.26.221.100 = 10111100. 00011010. 11011101. 01100100
255.255.255.240=11111111. 11111111. 11111111. 11110000 (Subnet bits)
188 . 26 . 221 . 96
NOTE: Anytime a 255 is in the subnet mask, the octet it is associated with, will be the number of the octet…….just do the Boolean “and” math to prove it! The only “real” work you have to do is based on the Octet of Interest (OOI), or the last octet which subnet bits are borrowed from.
____________________________________________________________________________________
1.) 188.26.221.100 255.255.255.240 Class: B # of Bits taken: 8+4=12 Network ID: 188.26.0.0
128 192 224 240 248 252 254 255
128 64 32 16 8 4 2 1
Subnet ID: 188.26.221.96 (0 and 0 = 0; 0 and 1 = 0; 1 and 0 = 0; 1 and 1 = 1)
Octet of Interest: 4
01100100
11110000
01100000=96
---------------------------------------------------------------------------------------------------------------------------------------------------
Magic number method using 1.) 188.26.221.100 255.255.255.240 from Exercise 3 for example.
1. Determine the class (A = 0-127; B = 128-191; C = 192-223) by looking at the first octet. Look at the following IP address: 188.26.221.100; this IP is a class B address because the first octet is 188 (it is in the range of 128-191). Because it is a class B address, the first two octets are dedicated to network bits (255.255.0.0).
2. Determine the bits for the subnet.
255.255.255.240 = is a class B address (class B = 255.255.0.0). Look at the remaining bits used in the subnet octets. In this case, we are using 8 bits from the third octet (255) and four bits from the fourth octet (240), a total of 12 bits. See below: we are using 12 bits as counted from the left.
3rd Octet 4th Octet
128 192 224 240 248 252 254 255 128 192 224 240 248 252 254 255
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0  1 = network bit
0 = host bit
3. Determine subnetwork ID by using magic number. In this case the magic number is 16 because it is the place holder for the 12th host bit, the last network bit in the subnet mask (4th bit in the fourth octet) used for sub networking. Since the first subnetwork ID is 188.26.221.0, add 16 to the subnet until it encompasses the IP address.
188.26.221.16
188.26.221.32
188.26.221.48
188.26.221.64
188.26.221.80
188.26.221.96Note: 188.26.221.100 is between subnets 188.26.221.96 and
188.26.221.128 188.26.221.128. So 188.26.221.100 belongs to 188.26.221.96
Continue until it fills out the octet, in this case:
188.26.221.240
188.26.221.256 256 There is no 256 therefore the max value of any octet is
255, so the last subnet ID is 240
4a. Besides doing it like item 4 above, use 240 (subnet mask from the fourth octet) and subtract from 256 to get the magic number of 16. (256 – 240 = 16)
4b. Use the magic number of 16 and divide into the last octet of the IP address, in this case it is 100. 100/16 = 6.25. Use the whole number 6 and multiply by 16, the magic number 6x16=96. 96 is the subnet ID, or the subnet ID is 188.26.221.96

## Slide 42: CIDR Notation
Classless Inter-Domain Routing (CIDR)
  A method of displaying how many bits are network (1) bits
  255.255.255.240 is the same as /28
    Network bits 1st octet: 8 bits, 2nd octet: 8 bits, 3rd octet: 8 bits, 4th octet: 4 bits
    8 + 8 + 8 + 4 = 28 network bits or /28
The 4th octet of a class A address
128
27
1
128
64
26
1
192
32
25
1
224
16
24
1
240
8
23
0
4
22
0
2
21
0
1
20
0
Value of binary
place holder
Subnet mask
number
Notes: Classless Inter-Domain Routing (CIDR)
CIDR, which stands for Classless Inter-Domain Routing, is an IP addressing scheme that improves the allocation of IP addresses. It replaces the old system based on classes A, B, and C. This scheme also helped greatly extend the life of IPv4 as well as slow the growth of routing tables.
Problems with class-based IP addressing
The old method of IP addressing came with inefficiencies that exhausted the availability of IPv4 addresses faster than it needed to. The classful routing system included classes A, B, and C:
Class A - Over 16 million host identifiers
Class B - 65,535 host identifiers
Class C - 254 host identifiers
The problem would commonly occur when an organization required more than 254 host machines and therefore would no longer fall into class C but rather class B. This means that the organization would use a class B license even though they had far less than 65,535 hosts. Therefore if an organization only required 2,500 hosts, they would be wasting about 63,000 hosts by holding a class B license which would greatly decrease the availability of IPv4 addresses unnecessarily.
How does CIDR work?
CIDR is based on variable-Length Subnet Masking (VLSM). This allows it to define prefixes of arbitrary lengths making it much more efficient than the old system. CIDR IP addresses are composed of two sets of numbers. The network address is written as a prefix, like you would see a normal IP address (e.g. 192. 55.25.0). The second part is the suffix which indicates how many bits are in the entire address (e.g. /12). Putting it together, a CIDR IP address would look like the following:
192.55.25.0 /28
The network prefix is also specified as part of the IP address. This varies depending upon the number of bits required. Therefore, taking the example above, we can say that the first 28 bits are the network part of the address while the last 4 bits are for host addresses. Or to put it another way; we have 28 network bits (binary 1’s) in the subnet mask and the remaining 4 bits are host bits (binary 0’s). Remember, we have four octets in the subnet mask, regardless of the class the IP address belongs to; we will have 28 network bits in a row, followed by 4 host bits for a total of 32 bit (four octets.)
CIDR: /28 = Subnet mask: 255.255.255.240 = binary: 11111111.11111111.11111111.11110000
Summary
CIDR is a great way to improve the efficiency of IP address distribution. It was vital with IPv4 as IP addresses were quickly being exhausted. IPv6 is now rolling out and although running out of IP address is now less of a problem, CIDR will continue to be used
Source: https://www.keycdn.com/support/what-is-cidr

## Slide 43: Classful vs Classless
Classful address
  Has not been subnetted
  Subnet mask same as default mask
    Class A = /8, Class B = /16, Class C = /24
Classless address
  Has been subnetted
  Must have CIDR notation or
  subnet mask to know what portion
  of address is network or host
Notes: Classful vs. Classless Addressing The main difference between classful and classless addressing is that classless addressing allows allocating IP addresses more efficiently than classful addressing.
Definition
Classful addressing is an IP address allocation method that allocates IP addresses according to five major classes. Classless addressing is an IP address allocation method that is designed to replace classful addressing to minimize the rapid exhaustion of IP addresses. Thus, this is the main difference between classful and classless addressing.
Usefulness
Another difference between classful and classless addressing is their usefulness. Classless addressing is more practical and useful than classful addressing.
Network ID and Host ID
In classful addressing, the network ID and host ID changes depending on the classes. However, in classless addressing, there is no boundary on network ID and host ID. Hence, this is another difference between classful and classless addressing.
Conclusion
Classful and classless addressing are two IP addressing types. The main difference between classful and classless addressing is that classless addressing allows allocating IP addresses more efficiently than classful addressing. In brief, classless addressing can avoid running out of IP addresses that can occur in classful addressing.
Why did we learn about classful IP addresses?
We learned classful IP addresses first, to create a foundation to build on. Everyone knows about class A, B & C and the subnet mask associated with each. The classful addresses will serve as our “starting point” for subnetting. If we are given a classful address, we will know where the network bits stop and where we can begin subnetting; or changing host bits into network bits to suit our network/host needs.
Source: https://pediaa.com/what-is-the-difference-between-classful-and-classless-addressing/

## Slide 44: IP Address Relationships
Network, subnet and host relationship
  An IP address supports one device
  Subnetting creates a range of IP addresses to support multiple devices
  Each device on a network will be associated with a particular subnet
11001111
207
00110110
.54
00000000
0
00010101
.21
11111111
255
10000000
.128
11111111
.255
11111111
.255
Network
Network
Host
Network
IP Address
Subnet Mask
One subnet bit
1
Notes: To start with, 207.21.54.0 is a class C address as determined by it’s first octet (192-223 = Class C). Because this is a class C address, automatically the first three octets (/24) are dedicated to network bits. Remember, we cannot change network bits…….Classful network bits are and will always be network bits! The fourth octet is dedicated to host bits. In this example one bit was subnetted to create two subnets. Each subnet contains 128 IP addresses (see slide 55)

## Slide 45: Subnet ID
Which subnet does the host belong to?
  207.21.54.35 255.255.255.128
00100011
.35
10000000
.128
4th Octet
1
0 127
128 255
128 255
0 127
Subnet
Mask
IP
Address
Subnet #1
Subnet ID: 207.21.54.0
Broadcast IP: 207.21.54.127
Subnet #2
Subnet ID: 207.21.54.128
Broadcast IP: 207.21.54.255
Notes: The host IP address 207.21.54.35 255.255.255.128 will be in one of two possible subnets. We know this because the first octet (207.) makes this a class C address or 255.255.255.0, but the subnet mask of 255.255.255.128 shows us that one host bit in the 4th octet has been subnetted.
Using the formula 2s = # of subnets; we can see that 21 = 2 subnets. The two subnets each have a range of 126 IP addresses.
Subnet #1 has a range of IP addresses of 207.21.54.0 – 127
Subnet #2 has a range of IP addresses of 207.21.54.128 – 255
Source: ICND1 100-105 pages 300-330

## Slide 46: Subnet ID
Which subnet does the host belong to?
  207.21.54.35 255.255.255.128
00100011
.35
10000000
.128
4th Octet
1
0 127
128 255
128 255
0 127
Subnet
Mask
IP
Address
Subnet #1
Subnet ID: 207.21.54.0
Broadcast IP: 207.21.54.127
Subnet #2
Subnet ID: 207.21.54.128
Broadcast IP: 207.21.54.255
Notes: The host IP address 207.21.54.35 255.255.255.128 will be in one of two possible subnets. We know this because the first octet (207.) makes this a class C address or 255.255.255.0, but the subnet mask of 255.255.255.128 shows us that one host bit in the 4th octet has been subnetted.
Using the formula 2s = # of subnets; we can see that 21 = 2 subnets. The two subnets each have a range of 126 IP addresses.
Subnet #1 has a range of IP addresses of 207.21.54.0 – 127
Subnet #2 has a range of IP addresses of 207.21.54.128 – 255
The host IP of 207.21.54.35 falls in the first subnet. Subnet ID: (first IP address) 207.21.54.0
(second IP address) 207.21.54.1
^
|
(Host IP address) 207.21.54.35
^
|
Broadcast IP: (last IP address) 207.21.54.127
Second subnet ID: (first IP address) 207.21.54.128
^
|
Broadcast IP: (last IP address) 207.21.54.255
Source: ICND1 100-105 pages 300-330

## Slide 47: Subnet ID
Are these two hosts on the same subnetwork?
  207.21.54.115 255.255.255.128
  207.21.54.129 255.255.255.128
10000000
.128
4th Octet
1
0 127
128 255
128 255
0 127
Subnet
Mask
Subnet #1
Subnet ID: 207.21.54.0
Broadcast IP: 207.21.54.127
Subnet #2
Subnet ID: 207.21.54.128
Broadcast IP: 207.21.54.255
Notes: Source: ICND1 100-105 pages 300-330

## Slide 48: Subnet ID
Are these two hosts on the same subnetwork?
  207.21.54.115 255.255.255.128
  207.21.54.129 255.255.255.128
10000000
.128
4th Octet
1
0 127
128 255
128 255
0 127
Subnet
Mask
Subnet #1
Subnet ID: 207.21.54.0
Broadcast IP: 207.21.54.127
Subnet #2
Subnet ID: 207.21.54.128
Broadcast IP: 207.21.54.255
Notes: 207.21.54.115 falls between 207.21.54.0 and 207.21.54.127 placing it on subnetwork: 207.21.54.0
207.21.54.129 falls between 207.21.54.128 and 207.21.54.255 placing it on subnetwork: 207.21.54.128
Source: ICND1 100-105 pages 300-330

## Slide 49: Class C: 2 Bit Mask /26
Because this is a class C address, all network devices will share the first three octets
  Can’t change Classful network bits!
11001111
207
00110110
.54
00000000
0
00010101
.21
11111111
255
10000000
.192
11111111
.255
11111111
.255
Network
Network
Host
Network
IP Address
Subnet Mask
Two subnet bits
11
Notes: Here we are converting two host bits into network bits.
We now have a subnet mask of 255.255.255.192 because a class C is naturally 255.255.255.0 the subnet mask of 255.255.255.192 was created because the first host bit we converted is valued at 128 and the second bit we converted is valued at 64 (128 + 64 = 192).
Using the formula 2s = # of subnets (22 = 4 subnets) we now have created 4 subnets. Using the formula (2h-2 = # of hosts) 26 -2 = 64 -2, we have 62 hosts for each of the four subnets we created.
Source: ICND1 100-105 pages 300-330

## Slide 50: Class C: 2 Bit Mask /26
Four subnets from two subnetted bits
  207.21.54.0 255.255.255.192
0
63
64
127
128
191
192
255
10000000
.192
4th Octet
11
2 subnetted bits
creates four subnets.
Each subnet has
64 IP addresses.
Subnet #1
Subnet ID: 207.21.54.0
Broadcast IP: 207.21.54.63
Subnet #2
Subnet ID: 207.21.54.64
Broadcast IP: 207.21.54.127
Subnet #3
Subnet ID: 207.21.54.128
Broadcast IP: 207.21.54.191
Subnet #4
Subnet ID: 207.21.54.192
Broadcast IP: 207.21.54.255
Subnet
Mask
Notes: Using the formula 2s = # of subnets (22 = 4 subnets)
First subnet, subnet #1 has the network ID: 207.21.54.0 and the range of IP addresses are .0 - .63
Second subnet, subnet #2 has the network ID: 207.21.54.64 and the range of IP addresses are .64 - .127
Third subnet, subnet #3 has the network ID: 207.21.54.128 and the range of IP addresses are .128 - .191
Fourth subnet, subnet #4 has the network ID: 207.21.54.192 and the range of IP addresses are .192 - .255
Using the formula 2h-2 = # of hosts (26 = 64 -2 = 62 hosts per subnetwork)
First subnet, subnet #1 has the host range of: 207.21.54.1 - .62
Second subnet, subnet #2 has the host range of: 207.21.54.65 - .126
Third subnet, subnet #3 has the host range of: 207.21.54.129 - .190
Fourth subnet, subnet #4 has the host range of: 207.21.54.193 - .254
Source: ICND1 100-105 pages 300-330

## Slide 51: Subnetting
Magic Number
  Groups of IP addresses come with each subnet mask
  Look at the binary value of
  the last subnet bit
128
27
1
128
64
26
1
192
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
Use the “Magic Number”
to determine the subnet IDs
- Add the magic # to previous
subnet ID to determine the
next subnet ID
OOI = Fist subnet ID will always be .0
Add Magic # (64) +64
2nd Subnet ID .64
3rd Subnet ID (+64) = .128
4th Subnet ID (+64) = .192
Notes: With every subnet mask, you will get a certain amount of IP addresses associated with it. In this example we converted we converted two host bits into network bits. When we look at the binary place holder value of the last network bit, we see a value of 64. When we convert two host bits into network bits, we get a subnet mask of 192 (128 + 64 = 192) and we will get 64 IP addresses for each subnet.
Using the binary place holder value of the subnet bit to calculate the answers to IP questions is often referred to as the “magic number.”
You can also determine the magic number by subtracting the subnet mask that has the last network bit from 256. NOTE: 256 = the number of possible IP addresses (.0 through .255)
Example for last subnet mask (192): 256
Subnet mask: - 192
Magic number: 64
The “magic number” is based on the binary value of the last bit converted to a subnet bit. Please note that we cannot use all the addresses in the range to assign to devices on your network.
Example: Using IP address 188.26.221.0 255.255.255.240 As usual we determine the class of the IP address by looking at the first octet. We see this is a class B address because the first octet, 188, falls between 128-191 (B class). The last subnet bit stops at 240 and the magic number for 240 is 16. This means we will get 16 IP addresses with this magic number.
3rd Octet 4th Octet
128 192 224 240 248 252 254 255 128 192 224 240 248 252 254 255
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
First subnet: 188.26.221.0  the first IP in the first subnet will be used for the Subnet ID
First host: 188.26.221.1  the first IP address that can be used for a device on the first subnet
Second host: 188.26.221.2  the second IP address that can be used for a device on the first subnet
Third host: 188.26.221.3  the third IP address that can be used for a device on the first subnet
V V V V V
V V V V V
V V V V V
Last host: 188.26.221.14  the fifteenth IP address that can be used for a device on the first subnet
Broadcast IP: 188.26.221.15  the last IP in the first subnet will be used for the Subnet Broadcast IP address
Second subnet: 188.26.221.16  the first IP in the second subnet will be used for the Subnet ID
First host: 188.26.221.17  the first IP address that can be used for a device on the second subnet
Second host: 188.26.221.18  the second IP address that can be used for a device on the second subnet
Third host: 188.26.221.19  the third IP address that can be used for a device on the second subnet
V V V V V
V V V V V
V V V V V
Last host: 188.26.221.30  the fifteenth IP address that can be used for a device on the second subnet
Broadcast IP: 188.26.221.31  the last IP in the second subnet will be used for the Subnet Broadcast IP address
The subnets will increase with increment of 16 (the magic number for subnet mask of 240) until the last subnet in the 4th octet:
Last subnet: 188.26.221.240  the first IP in the last subnet will be used for the Subnet ID
First host: 188.26.221.241  the first IP address that can be used for a device on the last subnet
Second host: 188.26.221.242  the second IP address that can be used for a device on the last subnet
Third host: 188.26.221.243  the third IP address that can be used for a device on the last subnet
V V V V V
V V V V V
V V V V V
Last host: 188.26.221.254  the fifteenth IP address that can be used for a device on the last subnet
Broadcast IP: 188.26.221.255  the last IP in the last subnet will be used for the Subnet Broadcast IP address
Source: ICND1 100-105 pages 300-330

## Slide 52: IP Address Allocation
Subnetting creates groups of IP addresses
  Each host bit converted into a network bit creates a range of IP addresses
  The first IP in a range is dedicated as the subnet ID
  The last IP in the range is dedicated as the broadcast IP
  Host range: IP addresses between the subnet ID and the broadcast IP
0 127
128 255
128 255
0 127
Subnet #1
Subnet ID: 207.21.54.0
First host: 207.21.54.1
Last host: 207.21.54.126
Broadcast IP: 207.21.54.127
Subnet #1
Subnet #2
Subnet #2
Subnet ID: 207.21.54.128
First host: 207.21.54.129
Last host: 207.21.54.254
Broadcast IP: 207.21.54.255
/25 or 255.255.255.128
Notes:   Each host bit converted into a network bit creates a range of IP addresses
  The first IP in a range is dedicated as the subnet ID
    Host bits are all 0’s and cannot be assigned to a device
  The last IP in the range is dedicated as the broadcast IP
    Host bits are all 1’s and cannot be assigned to a device
  The range of IP addresses between the subnet ID and the broadcast IP can be assigned to devices on the network

## Slide 53: Subnetting
Complete exercise #4
  First determine the IP address class
  Determine how many bits are required to create the amount of subnets requested
  Determine the subnet mask
  Determine the second subnet ID
  Determine the next to last subnet ID
10000000
.224
4th Octet
111
Subnet
Mask
0--31
224--255
32--63
192--224
Second subnet
Next to last subnet
Notes: Magic number method using 1.) from Exercise worksheet #4: 172.15.0.0 50 subnets requested
1. Determine the class (A = 0-127; B = 128-191; C = 192-223) by looking at the first octet. Look at the following IP address: 172.15.0.0; this IP is a class B address because the first octet is 172 (it is in the range of 128-191). Because it is a class B address, the first two subnet octets are dedicated to network bits (255.255.0.0).
2. Determine how many bits are needed to create the number of subnets required.
Example: to get 50 subnets, you will need 6 bits (26 = 64).
3. Determine the subnet mask. Take the 6 bits from the host bits to use as subnet bits:
128 64 32 16 8 4 2 1
128 192 224 240 248 252 254 255
1 1 1 1 1 1 0 0  252 will be the subnet mask for the 3rd octet
255.255.252.0 is the subnet mask (class B subnet + the 6 subnet bits).
4. Look for the magic number above the 252; it is 4. 4 will be the magic # for this network ID. Add the magic number to the network IP to identify the next subnet ID.
172.15.0.0  the network ID (and first subnetwork)
172.15.4.0  the next (second) subnet ID
5. Determine the next to last subnet by subtracting the magic # from the octet of interest in the subnet mask (252)
.252 – 4 = .248
The next to last subnet ID for 172.15.0.0 is 172.15.248.0
Note: The number in the OOI of your subnet mask will always be the last subnet for that octet. By subtracting the magic number from it; the sum will be the next to last subnet.
-----------------------------------------------------------------------------------------------------------------------
Wildcard method using 7.) from Exercise worksheet #4: 210.120.50.0 5 subnets requested
1. Identify the class of IP address, based on the first octet.
210.120.50.0  this is a class C network
2. Determine how many bits are needed to create the number of subnets required.
Example: to get 5 subnets, you will need 3 bits (23 = 8).
3. Determine the CIDR. Add the network and subnet bits together. This is a class C address using 24 network bits and then add the subnet bits (3) together to create the /27 total network bits.
4. Use the “Packetlife.net” document and find /27. Note the subnet mask and wildcard info.
CIDR Subnet Mask Wildcard
/27 255.255.255.224 0.0.0.31
5. Add 1 to the wildcard to get information required to determine the next subnet ID.
0.0.0.31 + 1 = 0.0.0.32
6. Determine the second subnet by adding the wildcard + 1 to the network ID:
210.120.50.0  network ID (1st subnet)
0 . 0 . 0 .32  wildcard + 1 (from step 5.)
210.120.50.32  is the second subnet ID
7. Determine the next to last subnet ID by going to the subnet mask octet of interest and look at the bit left to it. 255.255.255.224
128 64 32 16 8 4 2 1
128 192 224 240 248 252 254 255
1 1 1 0 0 0 0 0
8. The next to last subnet ID is 210.120.50.192
Note: to determine the wildcard of a subnet mask, all you have to do is subtract 255 from each subnet mask octet
Example 255.255.255.255 maximum number per octet
255.255.255.224  subnet mask
0 . 0 . 0 . 31  wildcard

## Slide 54: How Many Hosts?
If 62 hosts are required on the subnet, reserve 6 host bits by counting from the
right, always starting from the fourth octet. The subnet becomes the bit after the
last required host bit. In this example the subnet mask becomes 255.255.255.192
128
27
1
128
64
26
1
192
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
4th Octet
Subnet
Mask
Count host bits from
the right, starting at
the 4th octet
Notes: Similar to the previous exercise (exercise #4), we need to determine how many bits are required to support our requirement. Unlike the previous exercise, we are allocating bits to support the required amount of hosts instead of subnetworks. When we allocate bits to create subnetworks, we count bits from the left. It is the opposite for allocating bits for hosts – we count bits from the right.
Creating (X) number of subnets: convert host bits into network bits by counting from the left. Example: create 8 subnets (23 = 8 subnets) using a B class subnet mask
255 . 255 . 0 . 0
11111111.11111111.11100000.00000000 Note: 3 host bits changed to network bits

To create 8 subnets, take the first three host bits counting from the left to right 
Creating (X) number of hosts per subnet: reserve host bits to insure there are enough host bits to support (X) of hosts on each subnet by counting from the right. Example: insure 6 hosts per subnet (23 = 8 hosts -2) using a B class subnet mask
255 . 255 . 0 . 0
11111111.11111111.11111111.11111000 Note: 3 host bits changed to network bits

To reserves 6 hosts per subnet, count from the right to the left to insure there will be 6 hosts per network. 

## Slide 55: How Many Hosts?
If 9,000 hosts are required on the subnet, reserve 14 host bits by counting from the
right, starting from the fourth octet. The subnet becomes the bit after the last required
host bit. In this example the subnet mask becomes 255.255.192.0
128
27
0
64
26
0
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
4th Octet
Subnet Mask 11111111.11111111.11000000.00000000
Count host bits from the right, starting at the 4th octet
128
27
1
128
64
26
1
192
32
25
0
16
24
0
8
23
0
4
22
0
2
21
0
1
20
0
3rd Octet
255 . 255 . 192 . 0
Notes: Similar to the previous exercise (exercise #4), we need to determine how many bits are required to support our requirement. Unlike the previous exercise, we are allocating bits to support the required amount of hosts instead of subnetworks. When we allocate bits to create subnetworks, we count bits from the left. It is the opposite for allocating bits for hosts – we count bits from the right.
Creating (X) number of subnets: convert host bits into network bits by counting from the left. Example: create 8 subnets (23 = 8 subnets) using a B class subnet mask
255 . 255 . 0 . 0
11111111.11111111.11100000.00000000 Note: 3 host bits changed to network bits

To create 8 subnets, take the first three host bits counting from the left to right 
Creating (X) number of hosts per subnet: reserve host bits to insure there are enough host bits to support (X) of hosts on each subnet by counting from the right. Example: insure 9,000 hosts per subnet (214 = 16,384 - 2) using a B class subnet mask
255 . 255 . 192 . 0
11111111.11111111.11000000.00000000 Note: 2 host bits changed to network bits

To reserve at least 9,000 hosts per subnet, count from the right to the left to insure there will be at least 9,000 hosts per network. 

## Slide 56: First and Last Host
Determine the first and last host in the second subnet
  Subnet ID: 207.21.54.128 255.255.255.128 (range of 128 addresses)
    First address in the second subnet is the network ID: 207.21.54.128
    Second address is 207.21.54.128 + 1 = 207.21.54.129 first host address
    Last host address: 207.21.54.255 – 1 = 207.21.54.254last host address
    Last address is broadcast address: 207.21.54.255
Subnet #1
Subnet ID: 207.21.54.0
Broadcast IP: 207.21.54.127
Subnet #2
Subnet ID: 207.21.54.128
Broadcast IP: 207.21.54.255
0 127
128 255
128 255
0 127
Subnet #1
Subnet #2
Notes: Requested is the first and last host address on the SECOND subnet. This is determined by identifying the subnet ID of the second subnet (207.21.54.128) and adding 1. The first IP in a range of addresses will be the subnet ID. The next IP after the subnetwork ID will be the first IP we can use on a host with the subnet (207.21.54.128 + 1 = 207.21.54.129). To determine the last host IP address, look for the last IP address, this will be the broadcast IP for the subnetwork. Subtract 1 from the broadcast IP to get the last host address on the subnet (207.21.54.255 - 1 = 207.21.54.254).

## Slide 57: Subnetting
Complete exercise #5
  First determine the IP address class
  Determine how many bits are required for the amount of hosts requested
  Determine the subnet mask
  Determine the second subnet ID using the magic number
  Determine the first host address on the second subnet
  Determine the last host address on the second subnet
Notes: Using 1.) from Exercise worksheet #5: 25.0.0.0 1000 hosts required
1. Determine the class of the IP: 25.0.0.0 Class: A
2. Determine the host bits needed: 1000 (210 = 1,024) Host bits: 10
3. Determine the subnet mask by counting host bits from the right.
(3rd Octet and Octet Of Interest) (4th Octet)
128 64 32 16 8 4 2 1 128 64 32 16 8 4 2 1
128 192 224 240 248 252 254 255 128 192 224 240 248 252 254 255
1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0
 2 bits for host  8 bits for host
The subnet mask is 255.255.252.0 The subnet is created by default: we started by counting the bits needed for hosts by counting from the right, once we reached the amount of host bits (the “0” bits) needed, the remaining bits will become network bits. Therefore, the subnet mask is created by default.
The first octet exists as a .255 because it is a class A address, the first octet of a class A address will always be network bits. The second octet become subnetwork bits because they are turned on (they become “1” bits). The third octet, we have 6 bits being used as subnetwork bits. The last subnetwork bit is in the position of “252” and this is why the third octet has the subnetwork mask of .252 The last octet are all 0’s and that is why the 4th octet has the subnet mask of .0
4. Determine the second subnet. Add the magic number to the first subnet ID.
First network ID: 25.0.0.0
Magic number: 0.0.4.0
Second subnet 25.0.4.0
5. Determine the first host by adding 1 to the subnet ID: 25.0.4.0 + 1
The first host is 25.0.4.1
6. Determine last host by adding the magic number (4) to the second subnet ID. This gives the next subnet ID (the 3rd subnet), once the next subnet ID is known, subtract 2 IP addresses to get the last usable host IP for the previous subnet.
Second subnet: 25.0.4.0
Magic number: 0.0.4.0
Next (3rd) subnet: 25.0.8.0
Subtract 1: 25.0.8.0 – 1 = 25.0.7.255 The last IP in a subnet will be used as a broadcast IP for the previous subnet
Subtract 1 from the broadcast IP: 25.0.7.255 – 1 = 25.0.7.254 This is the last host IP on the second subnet.

## Slide 58: Subnetting
The IP address and the subnet mask relationship
  Control the subnet mask; control your network(s)
    Make subnetworks based on the number of networks needed
    Make subnetworks based on the number of hosts needed on each subnet

## Slide 59: Putting It All Together
Given an IP address and subnet mask determine:
  The network class
  The network bits
  The host bits
  The subnet ID
  The broadcast address
  The host range
Notes: Completing the tasks listed in this slide will demonstrate you understand the concepts of subnetting. All these items have already been explained, but now we will bring it all together to show you the “big picture” of subnetting.

## Slide 60: Putting It All Together
169.199.69.137 255.255.255.192
  What is the network class?
Notes: Always the very first thing to do is determine the class of the IP address given.

## Slide 61: Putting It All Together
169.199.69.137 255.255.255.192
  What is the network class? Class B
  What are the network bits?
  What are the subnet bits?
  How many subnets?
Notes: We already know this is a class B so the first two octets are required to be 255.255
What is the subnet mask in comparison to the class B subnet mask?

## Slide 62: Putting It All Together
169.199.69.137 255.255.255.192
  What are network bits? 26 = 16 network bits + 10 subnet bits
  What are the subnet bits? 10 bits
  How many subnets with 10 bits? 210 = 1,024 subnets
.11111111
.255
10101001
169
01000101
.69
10001001
.137
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
IP Address
Subnet Mask
11
10 subnet bits
Notes: We already know this is a class B address, so the first two octets are required to be 255.255
What is the subnet mask in comparison to the class B subnet mask? 10 bits are used to create subnets, 2s = # of subnets (210 = 1,024 subnets) using this information we can formulate there are 1,024 subnets.

## Slide 63: Putting It All Together
169.199.69.137 255.255.255.192
  What are the host bits?.11111111
  How many host per subnet?
.255
10101001
169
01000101
.69
10001001
.137
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
IP Address
Subnet Mask
11
Notes: We have already determined the network bits, so all we have to do now is to look at the remaining subnet mask bits – the remaining bits will be the host bits.

## Slide 64: Putting It All Together
169.199.69.137 255.255.255.192
  What are the host bits? 6 bits
  How many host per subnet? 26 = 64 – 2 = 62 hosts
10101001
169
01000101
.69
10001001
.137
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
IP Address
Subnet Mask
11
6 host bits
Notes: We have already determined the network bits, so all we have to do now is to look at the remaining subnet mask bits – the remaining bits will be the host bits. We have 6 bits for host addresses.
Use the formula: 2h – 2 = # of hosts per subnet; we have 26 – 2 = 62 hosts per subnet.

## Slide 65: Putting It All Together
169.199.69.137 255.255.255.192
  What is the subnet ID?
10101001
169
01000101
.69
10001001
.137
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
IP Address
Subnet Mask
11
Notes: What subnet does the host 169.199.69.137 belong to?

## Slide 66: Putting It All Together
169.199.69.137 255.255.255.192
  What is the subnet ID? 169.199.69.128
  Binary method: use Boolean “AND” math
  Magic number method
    Magic # 64 divided into Octet of Interest
    137/64 = 2 (use the whole number, dispose of the remainder)
    2 x 64 = 128
169.199.69.137: 1 0 1 0 1 0 0 1. 1 1 0 0 0 1 1 1. 0 1 0 0 0 1 0 1. 1 0 0 0 1 0 0 1
255.255.255.192: 1 1 1 1 1 1 1 1. 1 1 1 1 1 1 1 1. 1 1 1 1 1 1 1 1. 1 1 0 0 0 0 0 0
169.199.69.128: 1 0 1 0 1 0 0 1. 1 1 0 0 0 1 1 1. 0 1 0 0 0 1 0 1. 1 0 0 0 0 0 0 0
Boolean AND
Ip Address
Subnet Mask
Subnet ID
Notes: What subnet does the host 169.199.69.137 belong to? Using the binary method, all we have to do is use Boolean AND math and add the host IP address to its subnet mask.
We can also quickly determine a hosts subnet ID by using the magic number method. Determine the magic number based on the subnet masks’ Octet of Interest (OOI), in this case the OOI is 192 and this makes 64 the magic #. Divide the magic # into the OOI of the hosts IP address (137 divided by 64.) The quotient is 2 with a remainder of 9, dispose of the remainder and work with only the whole #. Multiply the whole number (2) with the magic # (64) to determine the hosts’ subnet ID.
137/64 = 2
2 x 64 = 128
Use 128 in the OOI of the IP address for the hosts’ subnet ID: 169.199.69.128

## Slide 67: Putting It All Together
169.199.69.137 255.255.255.192
  What is the broadcast address?
10101001
169
01000101
.69
10001001
.137
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
IP Address
Subnet Mask
11
Notes: What is the broadcast address for this host?

## Slide 68: Putting It All Together
169.199.69.137 255.255.255.192
  What is the broadcast address? 169.199.69.191
    Use the magic number of 64 and add to the subnet ID, then subtract 1
    Can also add wildcard to subnet ID (0.0.0.63 + 169.199.69.128 = 169.199.69.191)
Determine wildcard by subtracting subnet mask from 255.255.255.255
255.255.255.255
255.255.255.192 Subnet Mask
0 . 0 . 0 . 63 Wildcard Mask
Notes: What is the broadcast address for this host? Use the subnet ID and add the magic number to it. This provides the next subnet ID, to get the broadcast of the previous subnet, just subtract 1.
subnet ID: 169.199.69.128
Magic #: 64
Next subnet ID: 169.199.69.192
-1
Broadcast IP: 169.199.69.191
You can also add the wildcard to the subnet ID and get the broadcast address. The slide demonstrate how to determine the wildcard.
Subnet ID 169.199.69.128
Wildcard 0 . 0 . 0 . 63
Broadcast 169.199.69.191

## Slide 69: Putting It All Together
169.199.69.137 255.255.255.192
  What is the host range?
10101001
169
01000101
.69
10001001
.137
11000111
.199
11111111
255
11000000
.192
11111111
.255
11111111
.255
IP Address
Subnet Mask
11
Notes: What is the host range for this address?

## Slide 70: Putting It All Together
169.199.69.137 255.255.255.192
  What is the host range? 169.199.69.129 to 190
    Add 1 to the subnet ID to determine the first host on this subnetwork
    Subtract 1 from the broadcast address
Subnet ID: 169.199.69.128
+1
First host: 169.199.69.129
Broadcast: 169.199.69.191
- 1
Last host: 169.199.69.190
Notes: What is the host range for this address?
Once we know the first IP address (the Subnet ID) all we have to do is add (+1) to the subnet ID to determine the first IP address we can use for a host on the network.
Once we know the last ip address (the broadcast IP) all we have to do is subtract (-1) from the broadcast IP to determine the last IP address we can use for a host on the network.
After the first and last host IP addresses are know we can now see all the IP addresses available to us; we now know the host range.

## Slide 71: Putting It All Together
Given an IP address and subnet mask determine:
  The network class Class B
  The network bits 26 = 16 network + 10 subnet
  The host bits 6
  The subnet ID 169.199.69.128
  The broadcast address 169.199.69.191
  The host range 169.199.69. 129 - 190
Notes: To complete the tasks listed in this slide will demonstrate you understand the concepts of subnetting. All these items have already been explained, but now we will bring it all together to show you the “big picture” of subnetting.

## Slide 72: Putting It All Together
Complete exercise #6
  First determine the IP address class
  Determine the subnet ID
  Determine the broadcast address
  Determine the first & last host
Notes: Using 1.) from Exercise worksheet #6: 220.200.50.96 /28 subnet mask
Steps for completing Exercise 6: Magic # Method
1. Determine the class of the IP: 220.200.50.96 Class: C
2. Add 1 to the subnet ID to get the first host IP:
220.200.50.96
+ 1
220.200.50.97  First IP Address
3. Determine the magic #
/28 is using 28 network bits. A class C has 24 bits, therefore 4 bits were taken from the host bits (28 – 24 = 4)
128 64 32 16 8 4 2 1
128 192 224 240 248 252 254 255
1 1 1 1 0 0 0 0
4. Determine the next subnet ID by adding the magic # to the network ID.
220.200.50.96
0. 0. 0.16
220. 200.50.112  Next subnet ID
5. Subtract 1 from next subnet ID to get the broadcast IP address.
220. 200.50.112
- 1
220.200.50.111  Broadcast Address for subnet 220.200.50.96
6. Subtract 1 from broadcast IP to get the last host IP address.
220.200.50.111
- 1
220.200.50.110  Last IP Address for subnet 220.200.50.96
Steps for completing Exercise 6: Wildcard method (using #1 for example)
220.200.50.96 /28
1. Determine network class. Class C
2. Add 1 to the subnet ID to get the first host IP:
220.200.50.96
+ 1
220.200.50.97
3. Using packetlife.org document, look up wildcard information using the /28 reference. Alternate: subtract subnet mask from 255.255.255.255 to get wildcard.
/28 = wildcard 0.0.0.15
4. Determine broadcast address by adding wildcard to the subnet ID.
220.200.50.96
+ 0. 0. 0.15
220.200.50.111  Broadcast Address for subnet 220.200.50.96
5. Determine the last IP address by subtracting 1 from the broadcast IP.
220.200.50.111
- 1
220.200.50.110  Last IP Address for subnet 220.200.50.96

## Slide 73: Network Address Translation (NAT)
Network Address Translation (NAT)
  Enables devices using a private IP address to access public networks
  Helps reduce public IP address consumption
  Hides private addresses from outsiders
Private LAN using
private IP addresses
Public network using public IP address
Notes: What Is NAT?
Network Address Translation (NAT) is a way to map multiple local private addresses to a public one before transferring the information. Organizations that want multiple devices to employ a single IP address use NAT, as do most home routers.
How Does NAT Work?
Let’s say that there is a laptop connected to a home router. Someone uses the laptop to search for directions to their favorite restaurant. The laptop sends this request in a packet to the router, which passes it along to the web. But first, the router changes the outgoing IP address from a private local address to a public address.
If the packet keeps a private address, the receiving server won’t know where to send the information back to — this is akin to sending physical mail and requesting return service but providing a return address of anonymous. By using NAT, the information will make it back to the laptop using the router’s public address, not the laptop’s private one.
NAT Types
There are three different types of NATs. People use them for different reasons, but they all still work as a NAT.
1. Static NAT
When the local address is converted to a public one, this NAT chooses the same one. This means there will be a consistent public IP address associated with that router or NAT device. When using this type of NAT; if you have 5 different computers in your private network, you will need 5 different public IP addresses. This type of NAT does not conserve (public) IP addresses.
2. Dynamic NAT
Instead of choosing the same IP address every time, this NAT goes through a pool of public IP addresses. This results in the router or NAT device getting a different address each time the router translates the local address to a public address. By using a pool of (public) IP addresses, you will only need a few public IP addresses to support a private network consisting of many computers.
3. PAT
PAT stands for port address translation. It’s a type of dynamic NAT, but it bands all the devices in a private network to a singular public IP address. Organizations that want all their employees’ activity to use a singular IP address use a PAT; simply put, a single public IP address will support all the devices in the private network.
Why Use NAT?
NAT is a straightforward enough process, but what is the point of it? Ultimately, it comes down to conservation and security.
IP Conservation
IP addresses identify each device connected to the internet. The existing IP version 4 (IPv4) uses 32-bit numbered IP addresses, which allows for 4 billion possible IP addresses, which seemed like more than enough when it launched in the 1970s.
However, the internet has exploded, and while not all 7 billion people on the planet access the internet regularly, those that do often have multiple connected devices: phones, personal desktop, work laptop, tablet, TV, even refrigerators.
Therefore, the number of devices accessing the internet far surpasses the number of IP addresses available. Routing all of these devices via one connection using NAT helps to consolidate multiple private IP addresses into one public IP address. This helps to keep more public IP addresses available even while private IP addresses proliferate.
On June 6, 2012, IP version 6 (IPv6) officially launched to accommodate the need for more IP addresses. IPv6 uses 128-bit numbered IP addresses, which allow for exponentially more potential IP addresses. It will take many years before this process finishes; so until then, NAT will be a valuable tool.
NAT Security
Additionally, NAT can provide security and privacy. Because NAT transfers packets of data from public to private addresses, it also prevents anything else from accessing the private device. The router sorts the data to ensure everything goes to the right place, making it more difficult for unwanted data to get by. It’s not foolproof, but it often acts as the first means of defense for your device.
NAT also allows you to display a public IP address while on a local network, helping to keep data and user history private.
All of this might seem complicated in theory, but it’s even more so in the real world. IT professionals use NAT to secure their data and use several devices under the same IP – and everyone is interested in securing their data.
Source: https://www.comptia.org/content/guides/what-is-network-address-translation

## Slide 74: Port Address Translation (PAT)
Port Address Translation (PAT): a common type of NAT
  Uses ephemeral ports to convert many private IPs to one public IP
Notes: Port Address Translation (PAT), is an extension to network address translation (NAT) that permits multiple devices on a local area network (LAN) to be mapped to a single public IP address. The goal of PAT is to conserve IP addresses.
Most home networks use PAT. In such a scenario, the Internet Service Provider (ISP) assigns a single IP address to the home network's router. When Computer 10.0.0.1 logs on the Internet, the router assigns the client a port number, which is appended to the internal IP address. This, in effect, gives Computer 10.0.0.1 a unique address. If Computer 10.0.0.2 logs on the Internet at the same time, the router assigns it the same local IP address with a different port number. Although both computers are sharing the same public IP address and accessing the Internet at the same time, the router knows exactly which computer to send specific packets to because each computer has a unique internal address.
Source: https://www.techtarget.com/searchnetworking/definition/Port-Address-Translation-PAT
https://www.auvik.com/franklyit/blog/network-address-translation-port-address-translation/

## Slide 75: Variable Length Subnet Mask (VLSM)
Variable Length Subnet Mask (VLSM)
  Concept to efficiently create multiple subnets from a single subnet
    Uses more than one subnet mask – better to match the size of each subnet
  Blocks of addresses are not uniform in size
    Reduces the number of wasted IP addresses in each subnet
Subnet 1
Fixed Length
Subnet Mask
Subnet 2
Subnet 3
Subnet 4
Subnet 1
Variable Length
Subnet Mask
Subnet 2
Subnet 3
Subnet 4
Notes: Variable Length Subnet Mask (VLSM) occurs when a network needs multiple subnets but the administrator wants to minimize wasting IP addresses. Subnetting up to now has kept all the blocks of IP addresses uniform in size. If an administrator is given a class C address and she needs four networks, subnet 1 needs to support 60 hosts, subnet 2 needs to support 10 hosts and subnets 3 and 4 only need to support 2 hosts. The administrator is required to subnet 2 host bit to create 4 subnets that can support 1 subnet needing 60 hosts. On subnet 2, over 40 addresses are being wasted. On subnets 3 and 4, over 50 addresses are being wasted on each network!
Advantages of VLSM over Fixed Length Subnet Mask (FLSM) –
1. In Fixed length subnet mask subnetting (FLSM), all subnets are of equal size and have equal number of hosts but in VLSM the size is variable and it can have variable number of hosts thus making the IP addressing more efficient by allowing a routed system of different mask length to suit requirements.
2. In FLSM there is a wastage of IP addresses but in VLSM there is a minimum wastage of IP addresses.
3. FLSM is preferred for private IP addresses while for public IP addresses VLSM is the best option.
VLSM provides a means not to waste all the addresses while giving the administrator flexibility. VLSM is used in both public and private networks.
Source: CCNA ICND1 100-105 pages 307-8

## Slide 76: Variable Length Subnet Mask (VLSM)
Efficient use of IP addresses
Router
Router
Router
Router
Need: 50
addresses
each
Need: 200
addresses
each
Need: 2
addresses
each
Given IP 172.160.24.0 /21
use VLSM to subnet.
Requirements
1 subnet for 200 hosts
3 subnets for 2 hosts
3 subnets for 50 hosts
Notes: To use VLSM we determine the amount of host bits required for each network. Then we place them in descending order from largest to smallest. Doing this insures we have enough host bits for the largest networks. Based on the host bits required, we then determine the CIDR notation. Determine the next subnet ID.
(see CCNA ICND1 100-105 pages 307-8)

## Slide 77: Variable Length Subnet Mask (VLSM)
How to subnet using VLSM
  1. Place in descending order, the largest network to the smallest
  2. Determine the amount of host bits required for each network
  3. Determine the CIDR notation/subnet mask for each network
  4. Determine the wildcard for each network
  5. Starting with the first network, add wildcard to network ID to get
  broadcast IP for network
  6. Add 1 to broadcast IP to determine next subnet ID
    Repeat step 5 and 6 for remaining subnets
Notes: To use VLSM we determine the amount of hosts required for each network. Then we place them in descending order from largest to smallest. Doing this insures we have enough host bits for the largest networks. Based on the host bits required, we then determine the CIDR notation. Determine the next subnet ID.
(see CCNA ICND1 100-105 pages 307-8)
1. Arrange the requirements in order from largest to smallest.
Networks in descending order
200
50
50
50
2
2
2
2. Determine the amount of host bits required to create the minimum amount of IP addresses for each requirement. Remember, two extra IP address are required to be used, one for the Subnet ID and one for subnet broadcast IP.
# of hosts + 2 more IPs for each network (Subnet ID and Broadcast IP)
Total # of IP # of host bits
200 + 2 = 202 8 bits will provide 256 ip addresses (supports 254 hosts)
50 + 2 = 52 6 bits will provide 64 ip addresses (supports 62 hosts)
50 + 2 = 52 6 bits will provide 64 ip addresses (supports 62 hosts)
50 + 2 = 52 6 bits will provide 64 ip addresses (supports 62 hosts)
2 + 2 = 4 2 bits will provide 4 ip addresses (supports 2 hosts)
2 + 2 = 4 2 bits will provide 4 ip addresses (supports 2 hosts)
2 + 2 = 4 2 bits will provide 4 ip addresses (supports 2 hosts)
3. Determine the CIDR notation by subtracting the required host bits (from step 2) from the total subnet mask bits (total of 32).
Networks Host Bits CIDR
200 8 host bits = /24 (32 total bits - 8 host bits = 24 network bits or “/24”)
50 6 host bits = /26 (32 total bits - 6 host bits = 26 network bits or “/26”)
50 6 host bits = /26 (32 total bits - 6 host bits = 26 network bits or “/26”)
50 6 host bits = /26 (32 total bits - 6 host bits = 26 network bits or “/26”)
2 2 host bits = /30 (32 total bits - 6 host bits = 30 network bits or “/30”)
2 2 host bits = /30 (32 total bits - 6 host bits = 30 network bits or “/30”)
2 2 host bits = /30 (32 total bits - 6 host bits = 30 network bits or “/30”)
4. Find the wildcard information on the Packetlife.net document using the CIDR notation (from step 3).
Networks CIDR Wildcard
200 /24 0.0.0.255
50 /26 0.0.0.63
50 /26 0.0.0.63
50 /26 0.0.0.63
2 /30 0.0.0.3
2 /30 0.0.0.3
2 /30 0.0.0.3
5. Determine the broadcast IP address by adding the wildcard to the subnet ID.
-- Start with the given IP address: this will be your first subnet ID
--- Given IP 172.160.24.0 /16
6. Add 1 to broadcast IP to get the next subnet ID
-- Repeat for remaining networks
Networks Subnet ID Wildcard Broadcast IP Next Subnet ID
200 172.160.24.0 + 0.0.0.255 172.160.24.255 +1 = 172.160.25.0
50 172.160.25.0 + 0.0.0.63 172.160.25.63 +1 = 172.160.25.64
50 172.160.25.64 + 0.0.0.63 172.160.25.127 +1 = 172.160.25.128
50 172.160.25.128 + 0.0.0.63 172.160.25.191 +1 = 172.160.25.192
2 172.160.25.192 + 0.0.0.3 172.160.25.195 +1 = 172.160.25.196
2 172.160.25.196 + 0.0.0.3 172.160.25.199 +1 = 172.160.25.200
2 172.160.25.200 + 0.0.0.3 172.160.25.203 +1 = 172.160.25.204

## Slide 78: Variable Length Subnet Mask (VLSM)
Efficient use of IP addresses
Router
Router
Router
Router
Need: 50
addresses
each
Need: 200
addresses
each
Need: 2
addresses
each
Given IP 172.160.24.0 /21 use VLSM
to subnet.
Requirement Subnet ID
200 (8 host bits) 172.160.24.0 /24
50 (6 host bits) 172.160.25.0 /26
50 (6 host bits) 172.160.25.64 /26
50 (6 host bits) 172.160.25.128 /26
2 (2 host bits) 172.160.25.192 /30
2 (2 host bits) 172.160.25.196 /30
2 (2 host bits) 172.160.25.200 /30
172.160.24.0 /24
172.160.25.192 /30
172.160.25.196 /30
172.160.25.200 /30
172.160.25.0 /26
172.160.25.64 /26
172.160.25.128 /26
Notes: To use VLSM we determine the amount of host bits required for each network. If it were not for VLSM either all the subnets would be large enough to support at least 200 hosts, or we would need 3 separate IP addresses to subnet one for 200 hosts, subnet another address for 3 subnets to support 2 hosts each and yet another IP to create 3 subnets supporting 50 host each.
(see CCNA ICND1 100-105 pages 307-8)

## Slide 79: VLSM Group Exercise
Complete VLSM Group Exercise
  1. Place in descending order, the largest network to the smallest
  2. Determine the amount of host bits required for each network
  3. Determine the CIDR notation/subnet mask for each network
  4. Determine the wildcard for each network
  5. Starting with the first network, add wildcard to network ID to get
  broadcast IP for network
  6. Add 1 to broadcast IP to determine next subnet ID
    Repeat step 5 and 6 for remaining subnets
Notes: Using 1.) from Exercise worksheet #6: 220.200.50.96 /28 subnet mask
Steps for completing Exercise 6: Magic # Method
1. Determine the class of the IP: 220.200.50.96 Class: C
2. Add 1 to the subnet ID to get the first host IP:
220.200.50.96
+ 1
220.200.50.97  First IP Address
3. Determine the magic #
/28 is using 28 network bits. A class C has 24 bits, therefore 4 bits were taken from the host bits (28 – 24 = 4)
128 64 32 16 8 4 2 1
128 192 224 240 248 252 254 255
1 1 1 1 0 0 0 0
4. Determine the next subnet ID by adding the magic # to the network ID.
220.200.50.96
0. 0. 0.16
220. 200.50.112  Next subnet ID
5. Subtract 1 from next subnet ID to get the broadcast IP address.
220. 200.50.112
- 1
220.200.50.111  Broadcast Address for subnet 220.200.50.96
6. Subtract 1 from broadcast IP to get the last host IP address.
220.200.50.111
- 1
220.200.50.110  Last IP Address for subnet 220.200.50.96
Steps for completing Exercise 6: Wildcard method (using #1 for example)
220.200.50.96 /28
1. Determine network class. Class C
2. Add 1 to the subnet ID to get the first host IP:
220.200.50.96
+ 1
220.200.50.97
3. Using packetlife.org document, look up wildcard information using the /28 reference. Alternate: subtract subnet mask from 255.255.255.255 to get wildcard.
/28 = wildcard 0.0.0.15
4. Determine broadcast address by adding wildcard to the subnet ID.
220.200.50.96
+ 0. 0. 0.15
220.200.50.111  Broadcast Address for subnet 220.200.50.96
5. Determine the last IP address by subtracting 1 from the broadcast IP.
220.200.50.111
- 1
220.200.50.110  Last IP Address for subnet 220.200.50.96

## Slide 80: IP addresses

## Slide 81: Student Individual Assistance
Student Individual Assistance (SIA)
  What is SIA
  It is a personalized tutor to meet your needs
  Lots of information to cover in Block III
    Study daily
    Ask for help

## Slide 82: Summary Objective 3
Objective: Relate Principles Pertaining to Internet Protocol (IP) Addressing and Subnetting.
  Evaluation
    Written Test / Training Mission
  Learning outcomes
    Explain the decimal, binary, & hexadecimal number systems & perform conversions
    Explain IPv4 addressing, classes, & perform subnetting
    Identify facts about & perform Variable Length Subnet Masking (VLSM)
    Identify facts about IPv6
    Identify facts about Network Address Translation (NAT)